## Slide 1
MASTER'S THESIS
OnDevice
Training
A Lightweight C Framework for Inference
& On-Device Training on MCUs
Mohamed Atef · 2026
~40
Source Files
C99
Language
MCU
Target Platform

## Slide 2
What Is This Codebase?
OnDeviceTraining is a pure-C, CMake-based framework that brings full neural network training (forward + backpropagation) to resource-constrained microcontrollers — not just inference.
Portability First
Same model code runs on MCU and PC host for debugging and reference
MCU Realism
Designed for tight RAM/Flash — static memory, no heap bloat
Incremental Design
Layers, quantization, and optimizers added without breaking baseline
Research Friendly
Clean abstractions to plug in custom training algorithms (FQT, RigL)
Planned Extensions
Gradient checkpointing QAT / mixed-precision Sparse training (RigL)

## Slide 3
System Architecture
USER API (InferenceApi · TrainingLoopApi · SgdApi · TensorApi)
TRAINING LOOP (CalculateGradsSequential · TrainingEpochDefault · TrainingBatch)
NN LAYERS (Linear · ReLU · Softmax · Conv1d · QuantizationLayer)
LOSS + OPTIMIZER (CrossEntropy · MSE · SGD / SGD-Momentum)
DATA PIPELINE (DataLoader · NPYLoader · CSVHelper)
TENSOR + QUANTIZATION (Tensor · DTypes · Quantization · TensorConversion)
ARITHMETIC PRIMITIVES (Matmul · Add · Mul · Div · Log · Rounding · Distributions)
Higher layers call into lower ones. UserAPI is the integration point for experiments.

## Slide 4
Core: Tensor & Quantization
tensor_t (core data primitive)
uint8_t* data
raw byte storage
shape_t* shape
N-dim size + order
quantization_t* q
precision config
sparsity_t* sparsity
sparsity mask (RigL hook)
parameter_t = tensor_t* param + tensor_t* grad
Quantization Modes
FLOAT32
Default FP32 — training baseline
SYM_INT32
Symmetric fixed-point, configurable max bits (FQT-style)
SYM (N-bit)
Symmetric N-bit integer with scale factor
ASYM (N-bit)
Asymmetric with scale + zero-point
INT32
Raw 32-bit integer (accumulator type)

## Slide 5
Core: Neural Network Layers
Linear
Linear.c / Linear.h
Fully-connected layer. Forward: Y = XWt + b. Backward: computes dL/dW, dL/db, dL/dX. Supports float and quantized paths.
ReLU
Relu.c / Relu.h
Element-wise activation. Forward: max(0,x). Backward: gradient mask where x > 0. Very low memory footprint.
Softmax
Softmax.c / Softmax.h
Normalized exponential output for classification. Backward fused with CrossEntropy for numerical stability.
Conv1d
Conv1d.c + Conv1dTransposed.c
1D convolution for audio/time-series features (e.g. MFCC-based speaker embeddings). Transposed version for up-sampling.
QuantizationLayer
QuantizationLayer.c
In-graph quantization layer: inserts fake quantize-dequantize ops so integer-aware gradients flow during backprop (FQT foundation).

## Slide 6
Core: Forward & Backward Pass
CalculateGradsSequential.c — the core training engine
1
Init Layer Outputs
Allocate activation tensors for each layer (correct shape + quantization config).
2
Forward Pass
Loop layers 0 to N calling forward(). Each reads from the previous activation.
3
Compute Loss
Apply CrossEntropy or MSE on final output vs. label. Returns scalar loss.
4
Init Grad Tensor
Allocate dL/d_output tensor with same shape as model output.
5
Backward Pass
Loop layers N to 0 calling backward(). Each propagates dL/d_input and updates dL/dW, dL/db.
6
Cleanup & Return
Free intermediate activations. Return trainingStats (loss + output copy).

## Slide 7
Optimizer, Loss & Data Pipeline
Optimizer (src/optimizer/)
SGD
Plain SGD: theta = theta - lr * grad
SGD-Momentum
v = beta*v + grad, theta = theta - lr * v
Loss Functions (src/loss_functions/)
CrossEntropy
Multi-class classification. Backward fused with Softmax for stability.
MSE
Mean Squared Error for regression. Backward: 2*(y_hat - y) / N
Data Pipeline (src/data_loader/ + src/csv/)
DataLoader
Wraps dataset into batches; supports shuffle, split, callback hooks
NPYLoader
Reads NumPy .npy files in C — bridge between Python preprocessing and C runtime
CSVHelper
Writes per-epoch training stats (loss, accuracy, F1) to CSV for Python/Excel analysis

## Slide 8
User API & Model Serialization
src/userApi/ — experiments call these functions, not the internals directly.
TensorApi
TensorApi.c
Allocate, free, copy, and init tensors with distributions (Xavier, zeros). Wraps internal storage management.
LinearApi / ReluApi / SoftmaxApi
layer/
High-level layer constructors binding parameters, quantization, and forward/backward hooks.
SgdApi / OptimizerApi
optimizer/
Creates optimizer instances bound to a model. Exposes step() and zero_grad() via function pointer table.
InferenceApi
InferenceApi.c
Single-function inference + loss calculation. Used during evaluation loops.
TrainingLoopApi
training_loop/
trainingRun() top-level loop. Calls epoch/batch helpers, collects loss/accuracy/F1, fires epoch callbacks.
StorageApi + Serialize
StorageApi.c / serial/
Serialize/deserialize model weights to binary files — saves trained models to flash on MCU.

## Slide 9
Relation to Your Thesis
Thesis Goal: FQT + RigL Sparse Training on STM32 Nucleo-F746ZG for LibriSpeech Speaker Identification
FQT (Fake Quantization Training)
Code entry point:
QuantizationLayer + Quantization.c
How it connects:
The QuantizationLayer and SYM_INT32/ASYM qtypes implement fake-quantize-dequantize in-graph. Weights and activations are quantized on the forward pass, but gradients flow through — the core FQT mechanism described by Deutel.
RigL (Dynamic Sparse Training)
Code entry point:
sparsity_t in Tensor.h + CalculateGradsSequential
How it connects:
The tensor already carries a sparsity_t field. The backprop engine propagates sparsity through layers. Your contribution: add a periodic RigL mask-update step — prune low-magnitude weights, regrow top-gradient weights.
Speaker ID on STM32
Code entry point:
Conv1d + TrainingLoopApi + Serialize
How it connects:
Conv1d supports MFCC-based audio feature extraction. TrainingLoopApi drives on-device adaptation. Serialize stores the model to flash. The no-heap static memory design targets STM32 RAM constraints directly.

## Slide 10
File Reading Sequence
Start from the bottom of the stack and work up — each file only uses what came before it.
1
src/common/include/Common.h
Macros: PRINT_DEBUG, PRINT_ERROR, reserveMemory. Every file depends on this.
2
src/tensor/include/Quantization.h + Quantization.c
Data types for precision: FLOAT32, SYM_INT32, ASYM. Read qtypes enum and configs.
3
src/tensor/include/Tensor.h + Tensor.c
Core primitive: tensor_t, shape_t, sparsity_t, parameter_t. Understand these deeply.
4
src/arithmetic/include/*.h + *.c
Matmul, Add, Mul, Div, Log, Rounding — the math kernels layers call.
5
src/layer/include/Layer.h + Linear.h/c + Relu.h/c + Softmax.h/c
Layer type enum, function pointers, three main trainable layers.
6
src/loss_functions/ + src/optimizer/
CrossEntropy, MSE (forward + backward); SGD optimizer step/zero.
7
src/data_loader/DataLoader.h/c + NPYLoader.h/c
How data enters the system — batches, samples, .npy file loading.
8
src/serial/ + src/userApi/tensor/ + layer/ + optimizer/
Model save/load (Serialize.c) and high-level API constructors.
9
src/userApi/training_loop/calculate_grads/CalculateGradsSequential.c
The actual backprop engine — forward pass, loss, backward loop in one function.
10
TrainingLoopApi.c → experiments/MnistExperiment.c
Full end-to-end training run. MnistExperiment.c is the best first experiment to read.

## Slide 11
Summary
OnDeviceTraining is a complete pure-C training framework (not inference-only) built for MCUs and PC hosts.
Architecture: 7-layer stack — arithmetic primitives up to a full training loop with loss, accuracy, F1, and confusion matrix.
FQT link: QuantizationLayer + SYM_INT32 tensors implement fake-quantization-aware training — the direct C base for your FQT experiments.
RigL link: sparsity_t in tensor_t is the structural hook for sparse masks. The backprop engine already propagates sparsity — your contribution adds the mask-update step.
Speaker ID link: Conv1d for audio features, Serialize for flash storage, TrainingLoopApi for on-device adaptation on STM32.
Read sequence: Common -> Tensor -> Arithmetic -> Layers -> Loss/Optim -> DataLoader -> UserAPI -> MnistExperiment
Mohamed Atef · Master's Thesis 2026