## Slide 1
UDE
UNIVERSITÄT
DUISBURG
ESSEN
Offen im Denken
On-Device Training for Edge AI
Combining Sparsity (RigL) and
Fully Quantized Training (FQT)
A literature-driven design for low-power microcontroller training
Master Thesis Review · Mohamed Elshorbagy
Target hardware: STM32 Nucleo-F746ZG · Application: LibriSpeech speaker identification
May 2026

## Slide 2
Overview
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
2
Agenda
01
Introduction & Motivation
Why on-device training matters, and what makes it hard
02
Background — Compression
Quantization and sparsity in modern deep learning
03
Sparse Training with RigL
Drop-and-grow dynamic sparse training (Evci et al., 2020)
04
Fully Quantized Training
Forward + backward pass quantization (Deutel et al., 2024)
05
Combining FQT and RigL
Memory and compute synergy on the same training loop
06
Hardware & Application
STM32 Nucleo-F746ZG running LibriSpeech speaker ID
07
Experimental Plan
Three phases — baselines → GPU integration → MCU port
08
Conclusion & Future Work
Where the contribution sits and what comes next

## Slide 3
Introduction
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
3
Why On-Device Training?
01
Privacy & Data Locality
Raw audio, biometrics, and health data never leave the device. Avoids regulatory exposure tied to cloud upload (GDPR, HIPAA).
02
Personalization
A model adapted to the user's voice, accent, or environment outperforms a generic one — and can keep adapting without re-deploying firmware.
03
Connectivity Independence
Useful for IoT nodes with intermittent or zero network access. Adaptation continues even when the cloud is unreachable.
04
Energy & Bandwidth Savings
Avoids transmitting large feature streams over wireless links — the radio is often the largest single energy consumer on an MCU.

## Slide 4
Introduction
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
4
The Two Resource Bottlenecks
Memory
Compute & Energy
■ Activations dominate during training, not weights
  ○ Backprop must store every layer's input until the gradient pass
  ○ Optimizer states (Adam m, v) double or triple weight footprint
■ MCU SRAM is typically 256–1024 KB total
  ○ STM32 F746ZG: 320 KB SRAM, 1 MB flash — every byte is fought for
■ Backprop ≈ 2× the FLOPs of inference
  ○ Forward + activation gradient + weight gradient passes
  ○ Floating-point MAC is 5–10× more energy than int8 MAC
■ Cortex-M7 @ 216 MHz ≈ 432 MFLOPS theoretical
  ○ No GPU, no DSP — every saved operation is energy saved

## Slide 5
Background
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
5
The Compression Landscape
Quantization
Reduce numeric precision
FP32 → int8 / int4 / fixed-point. Linear in compute and memory savings (4× from FP32 → int8). Universally applicable.
✓
Sparsity
Set most weights to zero
Unstructured (any weight) or structured (rows, blocks, channels). Compute saving needs sparse-aware kernels or hardware support.
✓
Knowledge Distillation
Train small student from large teacher
Reduces architecture cost — orthogonal to training-time savings. Doesn't help when training itself must run on the MCU.
Low-Rank Factorization
Decompose dense matrices
Common in transformers; less applicable to small MCU CNNs whose matrices aren't large enough to benefit.
This work focuses on Quantization + Sparsity applied during training, not after.

## Slide 6
Background
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
6
Quantization in One Slide
The Idea
Replace FP32 numbers with low-bit integers and a scale factor.
x_q = round(x / s) + z (scale s, zero-point z)
Benefits
■ 4× memory reduction (FP32 → int8); 8× for int4
■ Integer MAC is faster and far more energy-efficient on Cortex-M
■ CMSIS-NN provides tuned int8 kernels for MAC-heavy layers
Three Regimes
PTQ
Post-Training Quantization
Apply after training; may degrade accuracy.
QAT
Quantization-Aware Training
Simulate quantization in the forward pass.
FQT
Fully Quantized Training
Forward AND backward pass are quantized.
FQT is the only option when training itself runs on the MCU.

## Slide 7
Background
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
7
Sparsity in One Slide
■ Density d = fraction of non-zero weights; sparsity = 1 − d
  ○ A 90 % sparse layer keeps only 10 % of its weights
■ Why it works — deep nets are heavily over-parameterized
  ○ Lottery-ticket subnetworks (Frankle & Carbin 2019) reach dense accuracy
■ Where the savings come from
  ○ Memory: store indices + values only (CSR / bitmask)
  ○ Compute: skip multiplications by zero — needs kernel support
■ Pruning vs. sparse training
  ○ Pruning: train dense, then remove weights — high training cost
  ○ Sparse training: model is sparse from the start — lower training cost
Dense (d = 1.0)
Sparse (d ≈ 0.18)
Same parameter count, ~5× fewer ops.
Key Tension
Unstructured sparsity gives the best accuracy / parameter trade-off — but block-structured sparsity is easier to accelerate on a Cortex-M.

## Slide 8
Sparse Training
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
8
Static vs. Dynamic Sparse Training
Static Sparse Training
Dynamic Sparse Training
■ Choose mask once at initialization
  ○ Mask never changes during training
  ○ Examples: random pruning, magnitude pruning at init
■ Pros / Cons
  ○ + Simplest implementation, no overhead
  ○ − Stuck with a possibly-bad mask the entire run
■ Mask updated periodically during training
  ○ Drop weights that hurt loss; grow new ones where loss might fall
  ○ Examples: SET (with growth), DSR, RigL
■ Pros / Cons
  ○ + Discovers a better sparse subnetwork as training progresses
  ○ − Must store dense gradients on update steps
RigL is the dynamic-sparse-training method this thesis builds on.

## Slide 9
RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
9
Rigged Lottery (RigL) — Overview
Evci, Gale, Menick, Castro, Elsen — ICML 2020
"Rigging the Lottery: Making All Tickets Winners"
Goal: train at fixed sparsity S from scratch, matching dense accuracy.
Knob 1
Sparsity Distribution
How sparsity is allocated per layer
Erdős–Rényi-Kernel (ERK) — capacity scales with parameter pressure
Knob 2
Update Schedule
When the mask is refreshed
Cosine-decayed update fraction; mask frozen after T_end
Knob 3
Drop / Grow Criteria
Which weights leave, which enter
Drop smallest |W|, grow largest |∂L/∂W| among dormant weights
Crucially: total FLOPs stay roughly constant — no dense forward pass required.

## Slide 10
RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
10
Drop and Grow Mechanism
1
Drop
Remove the |W| smallest-magnitude active weights.
These contribute least to the forward pass and represent the lowest expected loss change if pruned.
2
Grow
Activate the same number of currently-zero weights with the largest |∂L/∂W|.
These are the connections the gradient signal says want to exist.
3
Reset
Newly-grown weights start at zero.
Dropped weights' optimizer state is discarded; freshly-grown weights start with fresh momentum.

## Slide 11
RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
11
Update Schedule and Sparsity Distribution
Update Schedule
Update fraction f_t controls how many connections swap at step t.
T_end
training step t
f_t
f_t = (α/2) · (1 + cos(π·t / T_end))
Updates every ΔT steps (typically 100–1000). After T_end the mask is frozen and training continues to convergence.
Erdős–Rényi-Kernel (ERK)
Per-layer density that adapts to layer geometry.
d_l ∝ (n_in + n_out + k_h·k_w) / (n_in · n_out · k_h · k_w)
▸
Smaller layers → more density
early conv layers, classifier head
▸
Larger layers → less density
middle conv blocks with high parameter count
Result: same global sparsity, much better accuracy than uniform allocation.

## Slide 12
RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
12
Why RigL Matters — Key Results
76.6 %
ResNet-50 top-1 accuracy at 80 % sparsity
(matches dense baseline)
5×
FLOPs reduction at 80 % sparsity
(vs. dense ResNet-50)
0
Extra dense forward passes
(sparsity preserved every step)
■ Outperforms iterative magnitude pruning at the same parameter budget
■ Beats static sparse training across all tested sparsities (50 % – 99 %)
■ Robust: works on CNNs (ResNet, MobileNet) and transformers
■ Limitation: still trains at full activation precision — no quantization integrated

## Slide 13
FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
13
Fully Quantized Training — Motivation
What gets quantized?
Weights
Activations
Backward
Optimizer
PTQ
Apply after training
✓
✓
—
—
QAT
Forward-pass simulation
✓
✓
—
—
FQT
Forward + backward + state
✓
✓
✓
✓
Why FQT is essential here
■ QAT only quantizes the forward pass — gradients stay FP32
  ○ Useless on an MCU that has no FP hardware budget for training
■ FQT quantizes weights, activations, AND gradients (typically int8)
  ○ Reference: Deutel et al. (2024), targeting Cortex-M with 256–512 KB SRAM
  ○ Outcome: training memory and FLOPs drop ~4×, with controlled accuracy loss

## Slide 14
FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
14
FQT — Forward Pass Quantization
■ Per-tensor symmetric int8 (Q8.x fixed-point on Cortex-M)
  ○ x_q = clip(round(x / s_x), −128, 127); s_x = max(|x|) / 127
  ○ Scales recomputed per mini-batch — captures activation distribution shift
■ Operator chain after quantization
  ○ y_int = (x_q − z_x) · (W_q − z_W) in int32 accumulator
  ○ Re-quantize: y = clip(round(y_int · s_x · s_W / s_y), −128, 127)
  ○ Bias added in int32 before re-quantization to avoid early clipping
■ Activation memory savings
  ○ Storing int8 activations cuts intermediate buffers 4× vs. FP32
  ○ Critical: backprop still needs them — int8 means 4× more layers fit
Quantized GEMM
x (FP32 activations)
Quantize → x_q (int8)
MatMul (int8 × int8 → int32)
+ bias (int32)
Re-quantize → y (int8)
Same MAC pipeline, 4× less memory.

## Slide 15
FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
15
FQT — Backward Pass Quantization
∂L/∂y
Incoming gradient
from the next layer
∂L/∂x
Input gradient
to the previous layer
∂L/∂W
Weight gradient
to the optimizer
All three must be quantized — but they don't behave like activations.
Two New Challenges
■ Wider dynamic range than activations
  ○ Need per-channel scales, not per-tensor
■ Quantization noise can bias the optimizer
  ○ Net effect compounds over thousands of steps
Mitigations (Deutel)
■ Stochastic rounding instead of round-to-nearest
  ○ Preserves gradient mean — see next slide
■ Per-channel int8 for gradients; per-tensor for activations
■ Higher bit-width (int16) for the gradient accumulator only

## Slide 16
FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
16
Stochastic Rounding — The Key Trick
■ Round-to-nearest is biased over many small updates
  ○ If |update| < ½ · LSB, every step rounds to zero
  ○ Net effect: model stops learning — "swamping"
■ Stochastic rounding: round up with prob = fractional part
  ○ E[round_stoch(x)] = x exactly — zero bias
  ○ Small updates accumulate correctly over time
  ○ Cost: one PRNG call per quantization
■ Why it matters here
  ○ FQT's int8 gradient accumulator would otherwise stall after warm-up
Definition
round_stoch(x) =
⌈x⌉ with prob. x − ⌊x⌋
⌊x⌋ with prob. ⌈x⌉ − x
Property
E[round_stoch(x)] = x
Implementation
draw u ∼ U(0,1)
return ⌊x⌋ + (u < frac(x))

## Slide 17
Integration
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
17
Combining FQT and RigL
FQT
Reduces precision
≈ 4× memory & compute / op
RigL
Reduces operation count
≈ 5× FLOPs at 80 % sparsity
+
=
≈ 20×
memory & compute saving
(upper bound vs. FP32 dense)
Why It's Non-Trivial
■ Grow step needs ∂L/∂W for currently-zero weights
  ○ Quantized gradients must keep enough precision to rank weights
■ Mask updates change which scales / zero-points are needed
  ○ Re-derive per-channel scales on update steps only
■ Sparse + quantized GEMM kernel doesn't exist off-the-shelf
Design Choices
■ Keep ∂L/∂W in int16 only on update steps; int8 otherwise
■ Custom sparse-GEMM writes directly to a quantized output buffer
■ Mask refresh aligned with mini-batch boundary — single sync point
  ○ Avoids stalling the int32 accumulator mid-batch

## Slide 18
Integration
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
18
Memory Budget (Indicative, per 256-unit FC layer)
Component
FP32 Dense
FQT Dense
FQT + RigL @ 80 %
Reduction
Weights
262 KB
65 KB
13 KB + indices
~16×
Activations
1024 B/sample × N
256 B/sample × N
256 B/sample × N
4×
Gradients (weights)
262 KB
65 KB (int8)
13 KB (sparse)
~16×
Optimizer state
524 KB (Adam m,v)
131 KB (int8 m,v)
26 KB (sparse)
~20×
Total (per layer)
~1 MB
~256 KB
~50 KB + masks
~20×
Numbers are illustrative for a 256×256 fully-connected layer; real STM32 budget will be measured experimentally.
From ~1 MB → ~50 KB per layer puts a 5–10 layer model inside a 320 KB MCU.

## Slide 19
Hardware
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
19
Target: STM32 Nucleo-F746ZG
Specifications
Core
Arm Cortex-M7 @ 216 MHz
FPU
Single-precision FPU + DSP
Flash
1 MB
SRAM
320 KB (256 KB + 64 KB)
Cache
16 KB I-cache + 16 KB D-cache
FLOPS
~432 MFLOPS theoretical (FP32)
I/O
Ethernet, USB, UART, multiple ADCs
Power
~150 mW typical at full load
What the Hardware Forces
■ 320 KB SRAM is the hard limit
  ○ Model + activations + grads + optimizer state must all fit
■ FPU exists but is too slow for full backprop in real time
  ○ Integer arithmetic via CMSIS-NN is preferred
■ No GPU, no DMA-accelerated sparse kernels
  ○ Roll our own sparse matmul or accept structured sparsity
■ Power budget: 100–200 mW
  ○ Every saved op directly extends battery life

## Slide 20
Application
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
20
LibriSpeech Speaker Identification
Task
Identify which of N enrolled speakers produced an audio segment — closed-set classification on LibriSpeech-clean (subset of speakers).
Pipeline
Mic
16 kHz audio
Pre-emphasis
25 ms / 10 ms
40-ch log-Mel
on-device FFT
3 conv blocks
global pool
FC head
N speaker logits
Why this fits the experiment
Right size
Speech features are stationary enough to run on a Cortex-M7.
Right use case
Speaker enrollment is a perfect on-device adaptation use case.
Right dataset
LibriSpeech provides clean, well-balanced labels for evaluation.

## Slide 21
Risk Assessment
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
21
Anticipated Risks & Mitigations
Risk
Mitigation
Severity
Accuracy collapse from compounding int8 errors
Stochastic rounding + per-channel grad scales + int16 accumulator on update steps
High
Sparse GEMM kernel slower than dense int8
Fall back to block-structured sparsity if unstructured doesn't beat dense
High
RigL grow step exceeds SRAM budget at update
Update one layer at a time; reuse a single dense scratch buffer
Medium
Mask updates desync with batch norm statistics
Freeze BN running stats during mask updates; recompute after T_end
Medium
LibriSpeech speaker-ID baseline tuning eats time
Lock the architecture early (3-block CNN); tune sparsity instead
Low

## Slide 22
Experimental Plan
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
22
Experimental Plan
Phase 1
Weeks 1–4
Baselines
FP32 dense, QAT-int8 dense, RigL FP32 dense — run on workstation GPU; measure top-1 accuracy at the same parameter / FLOP budget.
Phase 2
Weeks 5–10
FQT + RigL on GPU
Implement the combined training loop in PyTorch with simulated int8 ops; measure accuracy degradation vs. each technique alone.
Phase 3
Weeks 11–16
MCU Deployment
Port forward + backward kernels to CMSIS-NN on the Nucleo-F746ZG; measure peak SRAM, latency per training step, and energy per step.
Deliverable: working end-to-end prototype with results across the four conditions.

## Slide 23
Conclusion
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
04.05.2026
23
Conclusion and Future Work
Conclusion
Future Work
■ On-device training is bounded by activation memory more than by weight memory
■ Quantization saves FLOPs and per-op energy
■ Sparsity saves operation count itself
■ FQT + RigL are complementary — together they close the gap to MCU-scale budgets
■ Stochastic rounding is the linchpin that keeps low-precision gradients useful
■ Structured (block-sparse) RigL variants for friendlier MCU kernels
■ Int4 weights with int8 gradients — push memory savings further
■ Federated FQT-RigL: aggregate sparse quantized updates across devices
■ Energy benchmarking on STM32 vs. accuracy delta
■ Extension to keyword spotting and speaker verification (open-set)

## Slide 24
Thank you.
Questions, feedback, and pushback welcome.
Mohamed Elshorbagy · Universität Duisburg-Essen · May 2026
On-Device Training for Edge AI
Combining Sparsity (RigL) and Fully Quantized Training (FQT)