## Slide 1
MASTER'S THESIS
Fully Quantized Training meets RigL
Sparse-from-scratch int8 training on a Cortex-M7 microcontroller
int8
forward · backward · update
~80–90%
weight sparsity (RigL)
320 KB
SRAM budget on Nucleo-F746ZG
Mohamed · LibriSpeech speaker identification

## Slide 2
Why on-device training is hard
Three constraints that defeat naive approaches
1
Memory
Cortex-M7 (F746ZG): only 320 KB SRAM. A single FP32 activation tensor for a small CNN already exceeds half the budget. Backprop requires keeping forward activations until the backward pass — this is the dominant cost.
2
Compute & energy
No GPU. ~216 MHz scalar FPU, no SIMD beyond DSP extensions. Training is FLOP-bound; FP32 backward is ~3× the cost of forward. Energy budget on a battery-powered edge device makes long training sessions infeasible.
3
Storage & transfer
1 MB Flash. Weights for a useful model can saturate Flash before training even begins. Updating model weights also implies wear-leveling on Flash or staying resident in SRAM.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
2 / 20

## Slide 3
FQT — Fully Quantized Training
Deutel et al., 2024 — On-Device Training of Fully Quantized DNNs on Cortex-M
Core idea
End-to-end int8. Forward, backward, and weight-update arithmetic all execute in 8-bit integer — no FP16 fallback for gradients.
Per-tensor scales. Each tensor (weight, activation, gradient) carries a scalar fp scale s. Operations rescale to a common scale, then perform integer GEMM.
Dynamic partial gradient. Instead of updating every weight every step, FQT updates a top-k subset chosen by gradient magnitude — cuts backward FLOPs sharply.
Reported gains. ≈ 35% memory and ≈ 49% latency vs. FP32 training on Cortex-M0+/M4/M7 baselines.
Quantization model
Symmetric per-tensor int8
q = clip(round(x / s), -127, 127)
x' = q · s
Quantized GEMM
Y_int32 = X_int8 · W_int8
Y_fp = (s_x · s_w) · Y_int32
Y_int8 = round(Y_fp / s_y)
Backward (custom int8 kernels)
dX_int8 = quant(dY · Wᵀ)
dW_int8 = quant(Xᵀ · dY)
SGD update (in-place int8)
W ← clip( W - quant(η · dW) )
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
3 / 20

## Slide 4
FQT — full algorithm
Per-iteration steps with dynamic partial gradient updates
Inputs : minibatch (X, y), int8 weights {W_l}, scales {s_w_l, s_a_l, s_g_l},
learning rate η, top-k fraction κ, layers l = 1..L
Output : updated weights
─────────────────────────────────────────────────────────────────────────
1. Quantize input batch: X̂ ← Q(X, s_a_0)
2. for l = 1..L // Forward
3. A_l ← Q( ϕ( DEQ(X̂_{l-1}) · DEQ(W_l) + b_l ), s_a_l )
4. cache(A_l) // needed for backward
5. ŷ ← softmax(A_L)
6. L ← CrossEntropy(ŷ, y); dA_L ← Q( ∂L/∂A_L , s_g_L )
7. for l = L..1 // Backward, all in int8
8. dW_l ← Q( A_{l-1}ᵀ · dA_l , s_g_l ) // weight grad
9. dA_{l-1} ← Q( dA_l · W_lᵀ , s_g_{l-1} ) // input grad
10. for l = 1..L // Dynamic partial gradient update
11. I_l ← TopK( |dW_l| , k = κ · |W_l| ) // indices to update
12. W_l[I_l] ← clip( W_l[I_l] - Q(η · dW_l[I_l]) , -127, 127 )
13. Refresh activation scales s_a_l using running max (every N steps)
Key trick (line 11): the top-k by gradient magnitude makes the backward pass O(κ·|W|) writes instead of O(|W|), giving Deutel's headline ~49% latency win.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
4 / 20

## Slide 5
RigL — Rigging the Lottery
Evci et al., 2020 — sparse-from-scratch dynamic mask training
Core idea
Sparse from scratch. No dense pretraining. A binary mask M is initialized at target sparsity s and refined during training.
Prune-then-grow. Every ΔT steps: drop a fraction f(t) of the smallest-magnitude active weights, then activate the same number of currently-masked weights with the largest gradient magnitudes.
Cosine schedule. f(t) = (α/2)·(1 + cos(π t / T_end)) — aggressive early, decays to zero so the topology stabilizes.
Why it wins. Magnitude tells you what to drop; the dense gradient tells you what would help if added. RigL matches dense accuracy at 80–90% sparsity on ImageNet.
Topology update at step t
M_t
Drop
M_{t+1}
Sparsity is preserved: |drop| = |grow|. Newly grown weights are initialized to 0.
f(t) = (α/2) · (1 + cos(π t / T_end)) // drop fraction
Update mask every ΔT steps until t = T_end
After T_end : freeze topology, finish training
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
5 / 20

## Slide 6
RigL — full algorithm
Per-iteration training with periodic mask updates
Inputs : weights W, target sparsity s, drop-rate α, end step T_end,
mask-update interval ΔT, training loader
─────────────────────────────────────────────────────────────────────────
1. Init mask M with sparsity s (Erdős–Rényi-Kernel per-layer dist.)
2. W ← W ⊙ M // zero pruned slots
3. for t = 1..T_train:
4. sample minibatch (X, y)
5. W_eff ← W ⊙ M
6. L ← Loss( f(X ; W_eff) , y )
7. g ← ∂L/∂W // dense gradient (full!)
8. W ← W - η · (g ⊙ M) // update only active weights
9. if t mod ΔT == 0 and t < T_end:
10. f_t ← (α/2) · (1 + cos(π t / T_end))
11. for each layer l:
12. k ← f_t · |active_l|
13. I_drop ← TopK_smallest( |W_l[M_l=1]| , k )
14. I_grow ← TopK_largest ( |g_l[M_l=0]| , k )
15. M_l[I_drop] ← 0; M_l[I_grow] ← 1; W_l[I_grow] ← 0
Note line 7: RigL needs the DENSE gradient at mask-update steps (to score inactive weights) — this is the expensive moment we must reconcile with FQT.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
6 / 20

## Slide 7
Why combine FQT and RigL?
Each technique fixes a different bottleneck
FQT alone
Makes int8 the entire pipeline (forward, backward, update).
Dynamic partial-gradient gives a one-time ~49% latency cut.
Still trains every weight in the dense topology — model size is bounded by Flash, not by what is useful.
RigL alone
Trains 80–90% fewer weights from scratch with little/no accuracy loss.
Demonstrated only in FP32; assumes a dense gradient is cheap to compute.
Requires a dense backward at mask-update steps — a hard fit on 320 KB SRAM.
Combined: int8 backward over a sparse, evolving mask
FQT shrinks each operation; RigL shrinks the operand. Together they target memory AND compute. The novel research question is whether the gradient signal that RigL needs to grow weights survives int8 quantization — i.e. whether |g|-rankings under FQT still pick useful connections.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
7 / 20

## Slide 8
Combined algorithm — FQT + RigL
What runs on the MCU at every iteration
Inputs : int8 weights W, mask M (target sparsity s), scales {s_w, s_a, s_g},
η, drop-rate α, T_end, ΔT, top-k κ for FQT partial update
─────────────────────────────────────────────────────────────────────────
1. for t = 1..T_train:
2. X̂ ← Q(X, s_a_0)
3. // ── Sparse-quantized forward ──────────────────────────────
4. for l = 1..L: A_l ← Q( ϕ( DEQ(A_{l-1}) · DEQ(W_l ⊙ M_l) ), s_a_l )
5. L_t ← CE(softmax(A_L), y); dA_L ← Q(∂L/∂A_L, s_g_L)
6. // ── Sparse-quantized backward ─────────────────────────────
7. for l = L..1:
8. dW_l ← Q( A_{l-1}ᵀ · dA_l , s_g_l ) // sparse-stored
9. dA_{l-1} ← Q( dA_l · (W_l ⊙ M_l)ᵀ , s_g_{l-1} )
10. // ── FQT dynamic partial weight update over active set ────
11. for l: I_l ← TopK_largest(|dW_l[M_l=1]|, κ·|active_l|)
12. W_l[I_l] ← clip(W_l[I_l] - Q(η · dW_l[I_l]))
13. // ── RigL mask update (every ΔT, t < T_end) ───────────────
14. if t mod ΔT == 0 and t < T_end:
15. compute g_dense_int8 (one-shot int8 backward, no mask) ⚠
16. f_t ← (α/2)(1 + cos(π t / T_end))
17. I_drop ← TopK_smallest(|W_l[M_l=1]|, f_t·|active_l|)
18. I_grow ← TopK_largest (|g_dense_int8[M_l=0]|, f_t·|active_l|)
19. M_l[I_drop]=0; M_l[I_grow]=1; W_l[I_grow]=0
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
8 / 20

## Slide 9
System view — what lives where
Memory map and per-tensor formats during one training step
SRAM (≤ 320 KB)
X̂ (mfcc)
int8 · per-tensor s_a_0
A_1
int8 · s_a_1
A_2
int8 · s_a_2
logits
int32 → softmax fp
dA_0
int8 · s_g_0
dA_1
int8 · s_g_1
dA_2
int8 · s_g_2
∂L/∂logits
int8 · s_g_L
W_l ⊙ M_l (stored sparse-CSR or bitmap)
int8 weights + 1-bit mask · per-channel s_w_l
Flash (1 MB)
Initial weights
Initial mask (RigL ER-K init)
MFCC feature bank
Speaker enrollment data
Trained weights are written back at end of training session (or held in SRAM if session is short).
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
9 / 20

## Slide 10
Python implementation — overview
What gets built on the workstation before any C is written
1
Environment & data
PyTorch 2.x + torchaudio. Download LibriSpeech dev-clean. Pick a closed-set of 40 speakers.
2
Feature pipeline
log-Mel filterbank or 13-MFCC, 25 ms / 10 ms, fixed 1 s window. Cache .npy tensors per-utterance.
3
Quantized model
Custom QLinear / QConv2d with fake-quant + STE; per-tensor symmetric int8; running min/max for activation scales.
4
RigL mask manager
Per-layer Mask object holding ER-K init, cosine-anneal drop fraction, ΔT update interval, prune-then-grow.
5
Training loop
Quantized forward → quantized backward → FQT partial-update step → every ΔT call mask manager.
6
Four-condition eval
FP32 dense, FQT dense, FP32+RigL, FQT+RigL — same seed, same data splits. Log accuracy, weight memory, FLOPs.
7
Export to C
Write weights_q8.c with int8 W, fp scales, packed 1-bit mask; emit a header with shapes + layer order.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
10 / 20

## Slide 11
Python — data & feature pipeline
Step 1–2: LibriSpeech → 13-MFCC tensors
import torch, torchaudio
from torchaudio.datasets import LIBRISPEECH
DS = LIBRISPEECH('./data', url='dev-clean', download=True)
SR = 16000; N_MFCC = 13; WIN = 25e-3; HOP = 10e-3; CLIP = 1.0
mfcc = torchaudio.transforms.MFCC(
sample_rate=SR, n_mfcc=N_MFCC,
melkwargs=dict(n_fft=400, hop_length=160, n_mels=40))
def extract(wave):
if wave.size(1) < SR: wave = F.pad(wave,(0, SR - wave.size(1)))
return mfcc(wave[:, :SR]) # [1, 13, 101]
speakers = sorted({m[3] for m in DS})[:40] # closed set
id_of = {sp:i for i,sp in enumerate(speakers)}
What this gives you
Fixed-shape tensors (1, 13, 101): trivial to feed a small Conv2d.
40-class closed-set: matches Deutel et al.'s benchmark size.
Cache extracted features as .npy to avoid re-running torchaudio every epoch — each utterance costs ~10 KB on disk.
Use a 80 / 10 / 10 train / val / test split over utterances, stratified by speaker.
Same split + seed for all four conditions (FP32, FQT, RigL, combined) — non-negotiable for fair comparison.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
11 / 20

## Slide 12
Python — quantized layer with STE
Step 3: a custom int8 Conv/Linear that PyTorch can autograd through
class QuantSTE(torch.autograd.Function):
@staticmethod
def forward(ctx, x, scale):
q = (x / scale).round().clamp_(-127, 127)
return q * scale
@staticmethod
def backward(ctx, g): return g, None # straight-through
class QLinear(nn.Module):
def __init__(self, fi, fo):
super().__init__()
self.W = nn.Parameter(torch.randn(fo, fi) * (1 / fi**0.5))
self.register_buffer('s_w', torch.tensor(0.05))
self.register_buffer('s_a', torch.tensor(0.05))
self.register_buffer('mask', torch.ones_like(self.W)) # RigL
def forward(self, x):
# update activation scale (EMA on running max)
with torch.no_grad():
self.s_a.mul_(0.99).add_(0.01 * x.abs().max() / 127)
Wq = QuantSTE.apply(self.W * self.mask, self.s_w)
xq = QuantSTE.apply(x, self.s_a)
return F.linear(xq, Wq)
Design notes
STE keeps the gradient path differentiable while the forward sees integer-valued tensors.
Mask is a Module buffer so RigL writes flow naturally with model.to(device).
Activation scale is updated via EMA on the running max → matches Deutel's per-tensor calibration.
QConv2d is the same pattern: replace F.linear with F.conv2d and use per-output-channel s_w if you want extra fidelity.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
12 / 20

## Slide 13
Python — RigL mask manager
Step 4: prune-and-grow as a single class hooked into the optimizer
class RigL:
def __init__(self, model, sparsity=0.9, alpha=0.3,
t_end=10_000, dt=200):
self.model, self.alpha = model, alpha
self.t_end, self.dt = t_end, dt
self._erk_init(sparsity)
def _erk_init(self, s):
for L in self.layers(): # ER-K init
density = (1 - s) * (L.W.numel() / max(L.W.shape))
keep = torch.rand_like(L.W) < density
L.mask.copy_(keep.float())
with torch.no_grad(): L.W.mul_(L.mask)
def step(self, t, dense_grads):
if t >= self.t_end or t % self.dt: return
f = 0.5 * self.alpha * (1 + math.cos(math.pi * t / self.t_end))
for L, g in zip(self.layers(), dense_grads):
k = int(f * L.mask.sum())
active = L.mask.bool()
drop = torch.topk(-(L.W[active]).abs(), k).indices
grow = torch.topk((g[~active]).abs(), k).indices
self._apply(L, drop, grow, active)
Hooks
1. On every iter, after backward, before optimizer.step(): zero out grads for masked weights.
2. Every ΔT iters, run an extra dense backward (no mask) and pass those gradients to RigL.step.
3. Re-zero W on freshly-grown indices so the optimizer state is clean.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
13 / 20

## Slide 14
Python — training loop & 4-condition eval
Steps 5–6: the experimental backbone of the thesis
rigl = RigL(model, sparsity=0.9) if USE_SPARSE else None
opt = torch.optim.SGD(model.parameters(), lr=1e-2, momentum=0.9)
for t, (xb, yb) in enumerate(loader):
logits = model(xb) # FQT forward
loss = F.cross_entropy(logits, yb)
loss.backward() # FQT backward
if USE_FQT: # partial update
for L in q_layers:
g = L.W.grad * L.mask
k = int(KAPPA * L.mask.sum())
top = torch.topk(g.abs().flatten(), k).indices
keep = torch.zeros_like(g).flatten()
keep[top] = 1
L.W.grad.mul_(keep.view_as(g))
if rigl: zero_pruned_grads(model)
opt.step(); opt.zero_grad()
if rigl and t % rigl.dt == 0:
with dense_grads(model, xb, yb) as g_dense:
rigl.step(t, g_dense)
Four conditions
A
FP32 dense
Upper-bound accuracy
B
FQT dense
Quantization cost
C
FP32 + RigL
Sparsity cost
D
FQT + RigL
The thesis claim
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
14 / 20

## Slide 15
C implementation — overview
What runs on the Nucleo-F746ZG after Python validates the design
1
Toolchain
STM32CubeIDE + ARM-GCC. Pull CMSIS-NN as a submodule for the int8 forward kernels we will reuse.
2
Model export
Dump weights_q8.c, scales.c, mask_bitmap.c from PyTorch → const arrays. Also a header with layer shapes and the order in which the runtime walks them.
3
Quantized forward
Re-use arm_convolve_s8, arm_fully_connected_s8 from CMSIS-NN. Wrap each with a mask-aware variant: zero-mask before MAC or use sparse-CSR layout.
4
Quantized backward
Hand-write int8 GEMMs for dW = AᵀdY and dX = dY Wᵀ. CMSIS-NN does not provide these; this is the bulk of the C work.
5
FQT partial update
Bounded min-heap of size κ·|active| to find the top-k weights to update; writes are in place against the int8 W.
6
RigL mask update
Two bounded heaps (smallest |W| over active, largest |g| over inactive); flip mask bits, zero new W slots.
7
Memory layout
Constants (W₀, M₀) in Flash; live A, dA, dW buffers double-buffered in SRAM with explicit per-layer reuse.
8
Profiling
DWT cycle counter for latency; on-board INA on Nucleo for energy; report against the host PyTorch baseline.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
15 / 20

## Slide 16
C — data structures
What gets written to flash and how the runtime walks it
// model_weights.h — emitted by the Python exporter
#define L_NUM 4
typedef struct {
int8_t *W; // weights, masked-out slots already zero
uint8_t *M; // packed 1-bit mask, ceil(N/8) bytes
float s_w; // weight scale
float s_a_in; // activation scale (input side)
float s_a_out; // activation scale (output side)
uint16_t fan_in;
uint16_t fan_out;
uint8_t kind; // 0=Conv 1=Linear 2=DepthwiseConv
} layer_t;
extern const layer_t LAYERS[L_NUM];
extern int8_t W0[ ... ]; // const, in flash
extern uint8_t M0[ ... ]; // const, in flash
// runtime mirrors in SRAM, copied at boot
extern int8_t W_ram[ TOTAL_W ];
extern uint8_t M_ram[ TOTAL_M_BYTES ];
extern int8_t dW_ram[ TOTAL_W ]; // gradient buffer
extern int8_t A_ram[2][ MAX_ACT ]; // double-buffered activations
Layout decisions
Mask format
1-bit packed bitmap. CSR is faster for inference but bitmap is far cheaper to update on a microcontroller.
Per-channel s_w?
Optional. Only worth it for Conv layers; Linear can stay per-tensor.
W in flash or SRAM?
Boot-time copy to SRAM so SGD writes don't wear out flash. Flash holds the immutable initialization.
Activations
Double-buffered (A_ram[0] / A_ram[1]); A_{l-1} freed once dW_l is computed.
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
16 / 20

## Slide 17
C — int8 kernels
Forward reuses CMSIS-NN; backward is custom
// Mask-aware forward (Linear)
void qfc_forward_masked(const layer_t *L,
const int8_t *x_in, int8_t *y_out)
{
for (int o = 0; o < L->fan_out; ++o) {
int32_t acc = 0;
for (int i = 0; i < L->fan_in; ++i) {
int idx = o * L->fan_in + i;
if (!bit_get(L->M, idx)) continue; // sparse skip
acc += (int32_t)x_in[i] * (int32_t)L->W[idx];
}
float yf = acc * (L->s_w * L->s_a_in);
y_out[o] = sat_int8(roundf(yf / L->s_a_out));
}
}
// Backward — dW and dX in int8
void qfc_backward(const layer_t *L,
const int8_t *x_in, // forward input
const int8_t *dy, // upstream grad
int8_t *dW_out, int8_t *dx_out)
{
const float s_g = L->s_a_out; // grad scale (proxy)
// dW = xᵀ · dy (mask applied)
for (int o = 0; o < L->fan_out; ++o)
for (int i = 0; i < L->fan_in; ++i) {
int idx = o * L->fan_in + i;
if (!bit_get(L->M, idx)) { dW_out[idx] = 0; continue; }
int32_t a = (int32_t)x_in[i] * (int32_t)dy[o];
dW_out[idx] = sat_int8(roundf(a * L->s_a_in / L->s_w));
}
// dx = dy · Wᵀ
for (int i = 0; i < L->fan_in; ++i) { /* analogous */ }
}
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
17 / 20

## Slide 18
C — partial weight update & mask update
FQT top-k SGD and RigL prune-grow, both running on the MCU
// FQT partial update — bounded min-heap of size k
void fqt_partial_update(layer_t *L, const int8_t *dW,
float eta, int k)
{
heap_t H; heap_init(&H, k); // min-heap by |dW|
int N = L->fan_in * L->fan_out;
for (int i = 0; i < N; ++i) {
if (!bit_get(L->M, i)) continue;
heap_push(&H, i, abs8(dW[i])); // O(log k) insert
}
for (int j = 0; j < H.size; ++j) {
int idx = H.idx[j];
int32_t step = (int32_t)roundf(eta * dW[idx]
* (L->s_w / L->s_a_in));
L->W[idx] = sat_int8((int32_t)L->W[idx] - step);
}
}
// RigL mask update on the MCU (every ΔT)
void rigl_update(layer_t *L, const int8_t *g_dense,
float drop_frac)
{
int active = popcount_bits(L->M, BITS_OF(L));
int k = (int)(drop_frac * active);
// 1) drop : k smallest |W| over active
heap_t Hd; heap_init(&Hd, k); // max-heap on |W|
for (int i = 0; i < N(L); ++i)
if (bit_get(L->M, i)) heap_push_max(&Hd, i, abs8(L->W[i]));
for (int j = 0; j < Hd.size; ++j) bit_clr(L->M, Hd.idx[j]);
// 2) grow : k largest |g_dense| over inactive
heap_t Hg; heap_init(&Hg, k); // min-heap on |g|
for (int i = 0; i < N(L); ++i)
if (!bit_get(L->M, i)) heap_push_min(&Hg, i, abs8(g_dense[i]));
for (int j = 0; j < Hg.size; ++j) {
bit_set(L->M, Hg.idx[j]);
L->W[Hg.idx[j]] = 0; // zero-init grown weight
}
}
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
18 / 20

## Slide 19
C — memory budget & deployment
Fitting a trainable model into 320 KB of SRAM
SRAM budget — 320 KB
W (int8) + masks (90 KB)
dW gradient buf (60 KB)
Activations (A0 / A1) (80 KB)
Heaps + scratch (30 KB)
Stack + system (60 KB)
Deployment steps
Flash header + initial weights to F746ZG via ST-Link.
USB-VCP serial channel for batch streaming + log retrieval.
DWT cycle counter on STM32 → per-step latency (μs).
Energy: external INA-219 on the 3.3 V rail.
Round-trip validation: identical (input, RNG seed) on PC ↔ MCU should produce bit-exact int8 weights for first N steps.
Targets to report in the thesis
Speaker-ID accuracy — vs. each of the 4 conditions
Per-step latency — ms / training step on F746ZG
Peak SRAM usage — snapshot at backward / mask update
Energy per epoch — mJ, from INA-219
Weight memory — KB on disk (sparse-stored int8)
FQT + RigL · On-Device Training · STM32 Nucleo-F746ZG
19 / 20

## Slide 20
Summary
FQT compresses every operation; RigL compresses the operand. Their intersection is the open question this thesis answers — and the implementation path runs from a PyTorch prototype directly to int8 sparse training on the F746ZG.
Key references
Deutel et al. (2024) — On-Device Training of Fully Quantized DNNs on Cortex-M Microcontrollers — int8 forward+backward+update with dynamic partial gradients.
Evci et al. (2020) — Rigging the Lottery: Making All Tickets Winners — sparse-from-scratch dynamic mask training (RigL).
Hoefler et al. (2021) — Sparsity in Deep Learning — taxonomy and background for the sparse-training literature.
LibriSpeech (Panayotov et al., 2015) — 1000-hour read-speech corpus; closed-set speaker ID benchmark used here.
CMSIS-NN (ARM, 2018+) — int8 neural-network kernels for Cortex-M; basis for the forward path on the F746ZG.
Mohamed · MSc Thesis · STM32 Nucleo-F746ZG