## Slide 1
UDE
UNIVERSITÄT
DUISBURG
ESSEN
Offen im Denken
MASTER'S THESIS · ON-DEVICE TRAINING
Fully Quantized Training
meets RigL
Sparse-from-scratch int8 training
on a Cortex-M7 microcontroller for closed-set speaker ID
int8
forward · backward · update
80-90%
weight sparsity (RigL)
320 KB
SRAM budget · F746ZG
Master Thesis Proposal · Mohamed Elshorbagy
Target hardware: STM32 Nucleo-F746ZG · Application: LibriSpeech speaker identification
May 2026

## Slide 2
Overview
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
2
Agenda
01
Why on-device training is hard
Memory, compute, and storage limits on Cortex-M class hardware
02
FQT — Fully Quantized Training
Deutel et al. 2024 — int8 forward, backward & update with partial gradients
03
RigL — sparse-from-scratch training
Evci et al. 2020 — prune-and-grow dynamic mask updates
04
Why combine FQT and RigL
Each technique fixes a different bottleneck — together they target memory AND compute
05
Combined algorithm — FQT + RigL
Per-iteration int8 sparse forward/backward with periodic mask refresh
06
System view on the F746ZG
Memory map, per-tensor formats, and what lives in SRAM vs. Flash
07
Python prototype
PyTorch reference — quantized layers, mask manager, 4-condition eval
08
C implementation & deployment
CMSIS-NN forward, hand-written backward, partial update, RigL on the MCU

## Slide 3
Introduction
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
3
Why on-device training matters
Four reasons that motivate moving training out of the cloud
01
Privacy & data locality
Raw audio, biometrics and health data never leave the device. Eliminates the cloud-transit attack surface and simplifies compliance with GDPR-style data-residency rules.
02
Personalization
A model adapted to the user's voice, accent or environment outperforms a one-size-fits-all server model. Real-time feedback (incorrectly transcribed names, noisy rooms) becomes training data the device can act on immediately.
03
Connectivity independence
Useful for IoT nodes with intermittent or no network access. The device keeps adapting even when offline — no cold-boot regression after a long disconnect.
04
Energy & bandwidth savings
Avoids transmitting large feature streams over wireless links. The radio is often the most expensive component to operate; shipping a gradient locally costs essentially nothing.

## Slide 4
Introduction
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
4
Why on-device training is hard
Three constraints that defeat naïve, cloud-style training
01
Memory
The F746ZG has only 320 KB of SRAM. A single FP32 activation tensor for a modest CNN can exceed half that budget. Backpropagation requires keeping forward activations alive until the backward pass — this is the dominant cost, not the weights themselves.
02
Compute & energy
No GPU. ~216 MHz scalar FPU with only DSP-extension SIMD. Training is FLOP-bound, and the FP32 backward pass is roughly 3× the cost of the forward. On a battery-powered edge device, long training sessions are thermally and energetically infeasible.
03
Storage & transfer
Only 1 MB of Flash. Weights for a useful model can saturate Flash before training even begins. Updating weights also implies either Flash wear-levelling or keeping the trained copy resident in SRAM between sessions.
320 KB
SRAM total budget
1 MB
Flash for weights + code
216 MHz
Cortex-M7 · FPU, no SIMD

## Slide 5
Background — FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
5
FQT — Fully Quantized Training
Deutel et al., 2024 — On-Device Training of Fully Quantized DNNs on Cortex-M
1
End-to-end int8
Forward, backward AND weight-update arithmetic all execute in 8-bit integer. No FP16 fallback for gradients — the entire training graph lives in int8.
2
Per-tensor scales
Each tensor (weight, activation, gradient) carries a scalar fp scale s. Operations rescale to a common scale, then run integer GEMM. Calibration uses a running max with an EMA so scales track distribution shift.
3
Dynamic partial gradient
Instead of updating every weight every step, FQT updates a top-κ subset ranked by gradient magnitude. This sharply reduces backward write traffic and dominates the latency win on M-class cores.
4
Reported gains
≈ 35 % memory and ≈ 49 % latency reduction versus FP32 training on Cortex-M0+ / M4 / M7 baselines, with negligible accuracy regression on the benchmarks Deutel et al. report.
Quantization & quantized arithmetic
# Symmetric per-tensor int8
q = clip(round(x / s), -127, 127)
x' = q * s
Quantized GEMM
Y_int32 = X_int8 @ W_int8
Y_fp = (s_x * s_w) * Y_int32
Y_int8 = round(Y_fp / s_y)
Backward + SGD update (in-place int8)
dX_int8 = quant(dY @ W.T)
dW_int8 = quant(X.T @ dY)
W = clip(W - quant(eta * dW))

## Slide 6
Background — FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
6
FQT — full per-iteration algorithm
Forward + int8 backward + dynamic partial weight update
Inputs : minibatch (X, y), int8 weights {W_l}, scales {s_w_l, s_a_l, s_g_l},
learning rate eta, top-k fraction kappa, layers l = 1..L
Output : updated weights
---------------------------------------------------------------------
1. Quantize input batch: X_hat <- Q(X, s_a_0)
2. for l = 1..L // Forward
3. A_l <- Q( phi( DEQ(X_hat_{l-1}) @ DEQ(W_l) + b_l ), s_a_l )
4. cache(A_l) // needed for backward
5. y_hat <- softmax(A_L)
6. L <- CE(y_hat, y); dA_L <- Q( dL/dA_L , s_g_L )
7. for l = L..1 // Backward, all in int8
8. dW_l <- Q( A_{l-1}.T @ dA_l , s_g_l ) // weight grad
9. dA_{l-1}<- Q( dA_l @ W_l.T , s_g_{l-1} ) // input grad
10. for l = 1..L // Dynamic partial gradient update
11. I_l <- TopK( |dW_l| , k = kappa * |W_l| ) // indices to update
12. W_l[I_l] <- clip( W_l[I_l] - Q(eta * dW_l[I_l]) , -127, 127 )
13. Refresh activation scales s_a_l using running max (every N steps)
Key trick (line 11): Top-k by gradient magnitude makes the backward pass O(kappa·|W|) writes instead of O(|W|) — this delivers Deutel's headline ~49% latency win.

## Slide 7
Background — FQT
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
7
FQT — line-by-line walkthrough
What each block of the FQT iteration does, in plain language
1
Quantize the input (line 1)
Each sample enters as fp32 audio features. We multiply by 1/s_a_0 and round to int8 once, so every downstream MAC is integer. After this line, no fp32 tensor crosses a layer boundary.
2
Quantized forward (lines 2–5)
For each layer: dequantize on the fly, run MAC + bias + activation, then re-quantize the output with the layer's s_a_l. Activations are cached because the backward pass needs them.
3
Loss & top gradient (line 6)
Softmax + cross-entropy at the final layer. The gradient dL/dA_L is quantized with s_g_L so the entire backward graph stays in int8.
4
Backward in int8 (lines 7–9)
Hand-coded GEMMs: dW = A.T @ dA gives the weight gradient; dA = dA_next @ W.T propagates the gradient to the previous layer. Both outputs are re-quantized to int8 immediately.
5
Top-κ partial update (lines 10–12)
Sort |dW_l| and keep only the κ·|W_l| largest. Update those weights in place, leave the rest unchanged. The trick — backward writes drop from O(|W|) to O(κ·|W|).
6
Refresh scales (line 13)
Activation scales s_a_l drift as the distribution shifts. Every N steps we update s_a_l from the running max; weight scales s_w_l can be left fixed for the whole run.

## Slide 8
Background — RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
8
RigL — Rigging the Lottery
Evci et al., 2020 — sparse-from-scratch dynamic mask training
1
Sparse from scratch
No dense pre-training. A binary mask M is initialised at the target sparsity (Erdős–Rényi-Kernel distribution per layer) and refined during training. Inference cost is the sparse cost from step 0.
2
Prune-then-grow
Every ΔT steps: drop a fraction f(t) of the smallest-magnitude active weights, then activate the same number of currently-masked weights with the largest gradient magnitudes. |drop| = |grow|, so sparsity is preserved exactly.
3
Cosine drop schedule
f(t) = (α/2)(1 + cos(π t / T_end)). Aggressive churn early, decaying to zero so the topology stabilises before final training. After T_end the mask is frozen and conventional sparse training continues.
4
Why it wins
Magnitude tells you what to drop; the dense gradient tells you what would help if added. RigL matches dense accuracy at 80–90 % sparsity on ImageNet — a regime where naïve magnitude pruning collapses.
Topology update at step t
M_t
drop smallest |W|
grow largest |g|
Legend
active
masked
dropped
newly grown (W=0)
Drop-fraction schedule
f(t) = (α/2) · (1 + cos(π · t / T_end))
update mask every ΔT steps, t < T_end
freeze topology after T_end and finish training

## Slide 9
Background — RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
9
RigL — full per-iteration algorithm
Sparse forward & sparse update, with a dense gradient only at mask-refresh steps
Inputs : weights W, target sparsity s, drop-rate alpha, end step T_end,
mask-update interval dT, training loader
---------------------------------------------------------------------
1. Init mask M with sparsity s (Erdos-Renyi-Kernel per-layer dist.)
2. W <- W * M // zero pruned slots
3. for t = 1..T_train:
4. sample minibatch (X, y)
5. W_eff <- W * M
6. L <- Loss( f(X ; W_eff) , y )
7. g <- dL/dW // dense gradient (full!)
8. W <- W - eta * (g * M) // update only active weights
9. if t mod dT == 0 and t < T_end:
10. f_t <- (alpha/2) * (1 + cos(pi * t / T_end))
11. for each layer l:
12. k <- f_t * |active_l|
13. I_drop <- TopK_smallest( |W_l[M_l=1]| , k )
14. I_grow <- TopK_largest ( |g_l[M_l=0]| , k )
15. M_l[I_drop] <- 0; M_l[I_grow] <- 1; W_l[I_grow] <- 0
Note line 7: RigL needs the DENSE gradient at mask-update steps (to score inactive weights) — this is the expensive moment we must reconcile with FQT on the MCU.

## Slide 10
Background — RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
10
RigL — line-by-line walkthrough
The five logical phases of one RigL iteration, explained
1
ER-K mask init (lines 1–2)
Each layer gets its target density via an Erdős–Rényi-Kernel distribution — bigger layers stay denser, smaller layers go sparser. W is masked once at t=0 so pruned slots start at exactly zero.
2
Normal sparse SGD (lines 3–8)
Same as a standard training step, but with two extras: the forward uses W*M, and the gradient applied to W is multiplied by M so inactive weights stay at zero.
3
Mask-refresh trigger (line 9)
Every ΔT steps, and only while t < T_end, the topology is allowed to change. After T_end the mask is frozen so the optimizer can converge on a fixed topology.
4
Cosine drop schedule (line 10)
f(t) starts at α (e.g. 0.3 = 30% of active weights drop) and decays smoothly to zero by T_end. Aggressive churn early; gentle later when the topology is stabilising.
5
Drop smallest |W| (lines 11–13)
For each layer, identify the k smallest-magnitude active weights — these are the ones already contributing the least, so dropping them costs almost nothing.
6
Grow largest |g| (lines 14–15)
From the currently-masked weights, pick the k with the largest dense gradient — these are the slots that would help most if added. Set mask=1 and weight=0 so they enter the network cleanly.

## Slide 11
FQT + RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
11
Why combine FQT and RigL?
Each technique fixes a different bottleneck — together they target memory AND compute
FQT alone
✓
Makes int8 the entire pipeline (forward, backward, update). Cuts memory and latency together.
✓
Dynamic partial-gradient gives a one-shot ~49% latency cut without changing the model topology.
✗
Still trains every weight in the dense topology — model size is bounded by what fits in Flash, not by what is useful.
RigL alone
✓
Trains 80–90% fewer weights from scratch with little or no accuracy loss versus the dense baseline.
✓
Inference cost is the sparse cost from step 0 — no dense pre-training, no expensive 'lottery ticket' search.
✗
Demonstrated only in FP32 and assumes a dense gradient is cheap. The required dense backward at mask-update steps is a hard fit on 320 KB SRAM.
Combined: int8 backward over a sparse, evolving mask
FQT shrinks every operation; RigL shrinks the operand. Together they target memory AND compute. The novel research question is whether the gradient signal RigL needs to grow weights survives int8 quantization — i.e. whether |g|-rankings under FQT still pick useful connections, and whether the dense backward at mask-refresh steps can be made affordable on a Cortex-M7.

## Slide 12
FQT + RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
12
Combined algorithm — FQT + RigL
What runs on the MCU at every iteration
Inputs : int8 weights W, mask M (target sparsity s), scales {s_w, s_a, s_g},
eta, drop-rate alpha, T_end, dT, top-k kappa for FQT partial update
---------------------------------------------------------------------
1. for t = 1..T_train:
2. X_hat <- Q(X, s_a_0)
3. // ---- Sparse-quantized forward ------------------------------
4. for l = 1..L: A_l <- Q( phi( DEQ(A_{l-1}) @ DEQ(W_l * M_l) ), s_a_l )
5. L_t <- CE(softmax(A_L), y); dA_L <- Q(dL/dA_L, s_g_L)
6. // ---- Sparse-quantized backward -----------------------------
7. for l = L..1:
8. dW_l <- Q( A_{l-1}.T @ dA_l , s_g_l ) // sparse-stored
9. dA_{l-1}<- Q( dA_l @ (W_l * M_l).T , s_g_{l-1} )
10. // ---- FQT dynamic partial update over the active set --------
11. for l: I_l <- TopK_largest(|dW_l[M_l=1]|, kappa * |active_l|)
12. W_l[I_l] <- clip(W_l[I_l] - Q(eta * dW_l[I_l]))
13. // ---- RigL mask update (every dT, t < T_end) ----------------
14. if t mod dT == 0 and t < T_end:
15. compute g_dense_int8 (one-shot int8 backward, no mask) *
16. f_t <- (alpha/2)(1 + cos(pi * t / T_end))
17. I_drop <- TopK_smallest(|W_l[M_l=1]|, f_t * |active_l|)
18. I_grow <- TopK_largest (|g_dense_int8[M_l=0]|, f_t * |active_l|)
19. M_l[I_drop]=0; M_l[I_grow]=1; W_l[I_grow]=0

## Slide 13
FQT + RigL
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
13
Combined FQT + RigL — walkthrough
Four sub-routines running together: forward, backward, partial update, mask update
A
Sparse-quantized forward (lines 2–5)
Quantize the input once. For each layer compute A_l = phi(DEQ(A_{l-1}) @ DEQ(W*M)). Multiplication by M physically skips the masked MACs — sparsity is real, not just zero-multiplied.
B
Sparse-quantized backward (lines 7–9)
Hand-coded int8 GEMMs. dW is only computed for the active slots (mask applied); dA propagates through (W*M).T. Storage stays sparse: dW lives in the same shape as W*M.
C
FQT partial update over active set (lines 11–12)
Within the |active| set, keep the top-κ by |dW|. Update those weights in place against int8 W. Both sparsity (RigL) AND top-k (FQT) prune the backward write set, multiplicatively.
D
RigL mask refresh — when triggered (lines 14–19)
On every ΔT-th step, do a one-shot dense int8 backward (no mask) to score inactive weights. Drop f(t)·|active| smallest |W|; grow f(t)·|active| largest |g_dense|; zero new W slots.
Open question: does the int8-quantized dense gradient at step D still pick the same useful connections that an fp32 RigL would have grown?

## Slide 14
System View
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
14
What lives where on the F746ZG
Memory map and per-tensor formats during one training step
SRAM · ≤ 320 KB
Activations (forward, kept for backward)
X_hat
int8 · s_a_0
A_1
int8 · s_a_1
A_2
int8 · s_a_2
logits
int32 → fp
Gradients (backward)
dA_0
int8 · s_g_0
dA_1
int8 · s_g_1
dA_2
int8 · s_g_2
dA_L
int8 · s_g_L
W_l * M_l (sparse-CSR or bitmap)
int8 weights + 1-bit packed mask
per-channel or per-tensor s_w_l (fp32 scalar each)
dW gradient buffer reuses one int8 tensor per layer
Flash · 1 MB
Initial int8 weights (W0)
Initial RigL mask (ER-K)
MFCC feature bank tables
Speaker enrolment metadata
Trained weights (write-back)
Trained weights write back at end of session.

## Slide 15
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
15
Python implementation — overview
What gets built on the workstation before any C is written
01
Environment & data
PyTorch 2.x + torchaudio. Download LibriSpeech dev-clean. Pick a closed-set of 40 speakers (matches Deutel et al.'s benchmark size).
02
Feature pipeline
13-MFCC, 25 ms / 10 ms hop, fixed 1 s window. Cache .npy per utterance to skip re-running torchaudio every epoch.
03
Quantized model
Custom QLinear / QConv2d with fake-quant + straight-through estimator; per-tensor symmetric int8; running-max EMA for activation scales.
04
RigL mask manager
Per-layer Mask buffer with ER-K init, cosine-annealed drop fraction, prune-and-grow at every ΔT steps.
05
Training loop
Quantized forward → quantized backward → FQT partial-update step → every ΔT call mask manager with an extra dense backward.
06
Four-condition eval
FP32 dense / FQT dense / FP32 + RigL / FQT + RigL — same seed, same data splits. Log accuracy, weight memory, FLOPs.
07
Export to C
Write weights_q8.c with int8 W, fp scales, packed 1-bit mask. Emit a header with shapes and the runtime layer order.
08
Bit-exact validation
Replay first N steps on the MCU with the same RNG seed; compare int8 weights byte-for-byte against the Python run.

## Slide 16
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
16
Data & feature pipeline
Step 1–2: LibriSpeech → 13-MFCC tensors of fixed shape
import torch, torchaudio
from torchaudio.datasets import LIBRISPEECH
DS = LIBRISPEECH('./data', url='dev-clean', download=True)
SR = 16000; N_MFCC = 13
WIN = 25e-3; HOP = 10e-3; CLIP = 1.0
mfcc = torchaudio.transforms.MFCC(
sample_rate=SR, n_mfcc=N_MFCC,
melkwargs=dict(n_fft=400,
hop_length=160,
n_mels=40))
def extract(wave):
if wave.size(1) < SR:
wave = F.pad(wave, (0, SR - wave.size(1)))
return mfcc(wave[:, :SR]) # [1, 13, 101]
speakers = sorted({m[3] for m in DS})[:40] # closed set
id_of = {sp:i for i,sp in enumerate(speakers)}
What this gives you
Fixed-shape tensor
(1, 13, 101) — trivial to feed a small Conv2d on the MCU.
40-class closed set
Matches Deutel et al.'s benchmark scope; cross-entropy stays well-conditioned.
Disk cache
Each utterance ≈ 10 KB on disk; recompute is the bottleneck without it.
Single seed
80 / 10 / 10 train-val-test split, stratified by speaker, shared across all 4 conditions.
Same split + seed across (FP32, FQT, RigL, combined) is non-negotiable for a fair comparison.

## Slide 17
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
17
Data pipeline — code walkthrough
What the LibriSpeech feature extractor does, function by function
1
Load LibriSpeech dev-clean
torchaudio's LIBRISPEECH wrapper downloads tar.gz on first run, then returns (waveform, sample_rate, transcript, speaker_id, chapter_id, utt_id) tuples — we need only speaker_id.
2
MFCC transform
13 cepstral coefficients per 25 ms frame with 10 ms hop, fed by a 40-mel filterbank over a 400-sample FFT. Same defaults Deutel et al. use for their keyword-spotting baseline.
3
extract() — pad to 1 s
Pad-then-truncate every utterance to exactly SR samples. The result is a fixed (1, 13, 101) tensor — the network sees uniform shapes, no dynamic axis.
4
Closed speaker set
Sort speaker IDs deterministically and take the first 40. id_of maps speaker → class index. The same set must be reused across all four experimental conditions.
5
Stratified split (not shown)
80/10/10 split over utterances, stratified by speaker — every speaker appears in train/val/test. Same RNG seed across the four conditions; otherwise comparisons are noise.
6
Disk cache
Each (1,13,101) tensor is ~10 KB on disk as .npy. Caching avoids re-running torchaudio every epoch — MFCC is the slowest call in the loop.

## Slide 18
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
18
Quantized layer with STE
Step 3: a custom int8 Linear/Conv that PyTorch can autograd through
class QuantSTE(torch.autograd.Function):
@staticmethod
def forward(ctx, x, scale):
q = (x / scale).round().clamp_(-127, 127)
return q * scale
@staticmethod
def backward(ctx, g): return g, None # straight-through
class QLinear(nn.Module):
def __init__(self, fi, fo):
super().__init__()
self.W = nn.Parameter(torch.randn(fo, fi) * fi**-0.5)
self.register_buffer('s_w', torch.tensor(0.05))
self.register_buffer('s_a', torch.tensor(0.05))
self.register_buffer('mask', torch.ones_like(self.W)) # RigL
def forward(self, x):
with torch.no_grad(): # EMA on running max
self.s_a.mul_(0.99).add_(0.01 * x.abs().max() / 127)
Wq = QuantSTE.apply(self.W * self.mask, self.s_w)
xq = QuantSTE.apply(x, self.s_a)
return F.linear(xq, Wq)
Design notes
STE backward
Keeps the gradient path differentiable while the forward sees integer-valued tensors.
Mask as buffer
RigL writes flow naturally with model.to(device); not optimised over.
EMA activation scale
Tracks distribution shift mid-training; matches Deutel's per-tensor calibration.
QConv2d twin
Same pattern with F.conv2d; per-output-channel s_w optional for extra fidelity.

## Slide 19
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
19
Quantized layer — code walkthrough
How QuantSTE and QLinear behave during forward and backward
1
QuantSTE.forward
Divide x by s, round and clamp to [-127, 127], then multiply back. The tensor is now visually fp32 but carries only int8-representable values — fake-quant, ready for a real int8 kernel substitution.
2
QuantSTE.backward
Returns the upstream gradient unchanged (g, None). This is the straight-through estimator — pretend the rounding never happened so gradients flow through. Standard and theoretically sound.
3
QLinear weights
W is a normal Parameter so SGD can update it. Initialised with 1/√fan-in variance — keeps post-MAC activations in a sensible range before the first calibration step.
4
Buffers: s_w, s_a, mask
Buffers move with model.to(device) but aren't trained. s_w is fixed per tensor; s_a follows the data; the RigL mask is written by an external manager — never by gradients.
5
EMA activation scale
Inside forward(), with no_grad: s_a ← 0.99·s_a + 0.01·|x|_max/127. Tracks distribution drift smoothly. Matches Deutel's per-tensor calibration.
6
Quantize-then-Linear
Both x and W·mask go through QuantSTE before F.linear, so the matmul sees integer-valued operands. Swapping in a real int8 kernel later requires no graph changes.

## Slide 20
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
20
RigL mask manager
Step 4: prune-and-grow as a single class hooked into the optimizer
class RigL:
def __init__(self, model, sparsity=0.9, alpha=0.3,
t_end=10_000, dt=200):
self.model, self.alpha = model, alpha
self.t_end, self.dt = t_end, dt
self._erk_init(sparsity)
def _erk_init(self, s):
for L in self.layers(): # ER-K init
density = (1 - s) * (L.W.numel() / max(L.W.shape))
keep = torch.rand_like(L.W) < density
L.mask.copy_(keep.float())
with torch.no_grad(): L.W.mul_(L.mask)
def step(self, t, dense_grads):
if t >= self.t_end or t % self.dt: return
f = 0.5 * self.alpha * (1 + math.cos(math.pi * t / self.t_end))
for L, g in zip(self.layers(), dense_grads):
k = int(f * L.mask.sum())
active = L.mask.bool()
drop = torch.topk(-(L.W[active]).abs(), k).indices
grow = torch.topk(( g[~active]).abs(), k).indices
self._apply(L, drop, grow, active)
Hooks into training
Every iter
After backward, before optimizer.step(): zero out grads for masked weights.
Every ΔT iters
Run an extra dense backward (no mask) and pass those gradients to RigL.step().
On grow
Re-zero W on freshly-grown indices and reset their optimizer state.

## Slide 21
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
21
RigL manager — code walkthrough
How the class hooks into PyTorch's training loop
1
__init__ takes the model
Stores references to the layers it manages, the cosine α, T_end (when to stop refreshing), and ΔT (how often). _erk_init runs once at construction.
2
_erk_init — ER-Kernel density
Per-layer density = (1-s) · (N/max(fan_in, fan_out)). Bigger layers keep more weights; tiny layers get a higher relative density so they don't collapse to zero connections.
3
step() — early exit
If t ≥ T_end (topology frozen) or t mod ΔT ≠ 0 (not a refresh step), return immediately. The hot path spends almost all iterations in this early-exit branch.
4
f(t) — drop fraction
Cosine schedule: 0.5·α·(1 + cos(π·t/T_end)). At t=0 returns α; at t=T_end returns 0. Smooth, no extra knobs once α is chosen.
5
Drop: smallest |W| over active
torch.topk on -(|W[active]|) picks the k weakest active weights. drop holds their indices (in the flattened active subspace).
6
Grow: largest |g| over inactive
torch.topk on |g[~active]| picks the k strongest masked weights by gradient. _apply flips mask bits, zeros W on grown slots, and clears optimizer momentum on those slots.

## Slide 22
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
22
Training loop & 4-condition eval
Steps 5–6: the experimental backbone of the thesis
rigl = RigL(model, sparsity=0.9) if USE_SPARSE else None
opt = torch.optim.SGD(model.parameters(), lr=1e-2, momentum=0.9)
for t, (xb, yb) in enumerate(loader):
logits = model(xb) # FQT forward
loss = F.cross_entropy(logits, yb)
loss.backward() # FQT backward
if USE_FQT: # partial update
for L in q_layers:
g = L.W.grad * L.mask
k = int(KAPPA * L.mask.sum())
top = torch.topk(g.abs().flatten(), k).indices
keep = torch.zeros_like(g).flatten()
keep[top] = 1
L.W.grad.mul_(keep.view_as(g))
if rigl: zero_pruned_grads(model)
opt.step(); opt.zero_grad()
if rigl and t % rigl.dt == 0:
with dense_grads(model, xb, yb) as g_dense:
rigl.step(t, g_dense)
Four experimental conditions
A
FP32 dense
Upper-bound accuracy reference.
B
FQT dense
Isolates the quantization cost.
C
FP32 + RigL
Isolates the sparsity cost.
D
FQT + RigL
The thesis claim — both at once.
Each condition reports: accuracy · weight memory (KB) · FLOPs/step · wall-clock training time.

## Slide 23
Python Prototype
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
23
Training loop — code walkthrough
The same loop runs all four conditions; flags select what is active
1
Optional RigL manager
Constructed only if USE_SPARSE. Same SGD optimizer for every condition — keeping the optimizer constant is what makes the four-way comparison legitimate.
2
Forward + loss + backward
Standard PyTorch three lines. Because QLinear is the layer type, the forward path is already quantized; loss.backward() computes the full int8 gradient through the STE.
3
FQT partial-update block
Only runs if USE_FQT. For each quantized layer, compute the κ·|active| largest |grad| over the mask-allowed slots and zero out every other gradient entry before opt.step().
4
Mask-zeroed gradients
zero_pruned_grads(model) sets g=0 on masked slots so they stay at zero through SGD. Cheaper than masking the weights themselves after each step.
5
opt.step + opt.zero_grad
Same as any PyTorch loop. The only weights that move are those whose gradients survived both the FQT top-k filter AND the RigL mask.
6
Periodic RigL refresh
Every ΔT iters: re-run forward+backward without the mask to get a dense gradient, then call rigl.step(t, g_dense). dense_grads() is a context manager that temporarily disables masking.

## Slide 24
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
24
C implementation — overview
What runs on the Nucleo-F746ZG after Python validates the design
01
Toolchain
STM32CubeIDE + ARM-GCC. CMSIS-NN pulled in as a submodule for the int8 forward kernels we reuse.
02
Model export
Dump weights_q8.c, scales.c, mask_bitmap.c from PyTorch → const arrays. Header file holds shapes and walk order.
03
Quantized forward
Reuse arm_convolve_s8 / arm_fully_connected_s8. Wrap each with a mask-aware variant: skip MAC or use sparse-CSR.
04
Quantized backward
Hand-written int8 GEMMs for dW = A^T dY and dX = dY W^T. CMSIS-NN does not provide these — bulk of the C work.
05
FQT partial update
Bounded min-heap of size κ·|active| selects top-k weights to update. Writes are in-place against the int8 W tensor.
06
RigL mask update
Two bounded heaps — smallest |W| over active, largest |g| over inactive. Flip mask bits, zero newly-grown slots.
07
Memory layout
Constants (W0, M0) in Flash. Live A, dA, dW buffers double-buffered in SRAM with explicit per-layer reuse.
08
Profiling
DWT cycle counter for latency; external INA-219 for energy. Reported against the host PyTorch baseline.

## Slide 25
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
25
C — data structures
What gets written to Flash and how the runtime walks it
// model_weights.h -- emitted by the Python exporter
#define L_NUM 4
typedef struct {
int8_t *W; // weights, masked-out slots zero
uint8_t *M; // packed 1-bit mask, ceil(N/8) bytes
float s_w; // weight scale
float s_a_in; // activation scale (input)
float s_a_out; // activation scale (output)
uint16_t fan_in;
uint16_t fan_out;
uint8_t kind; // 0=Conv 1=Linear 2=DWConv
} layer_t;
extern const layer_t LAYERS[L_NUM];
extern int8_t W0[ ... ]; // const, Flash
extern uint8_t M0[ ... ]; // const, Flash
// runtime mirrors in SRAM, copied at boot
extern int8_t W_ram [ TOTAL_W ];
extern uint8_t M_ram [ TOTAL_M_BYTES ];
extern int8_t dW_ram [ TOTAL_W ]; // gradient buffer
extern int8_t A_ram[2][ MAX_ACT ]; // double-buffered acts
Layout decisions
Mask format
1-bit packed bitmap. CSR is faster for inference but bitmap is far cheaper to update on an MCU.
Per-channel s_w
Optional. Only worthwhile for Conv layers; Linear stays per-tensor.
W in Flash or SRAM?
Boot-time copy to SRAM so SGD writes don't wear Flash. Flash holds the immutable init.
Activations
Double-buffered (A_ram[0]/[1]); A_{l-1} is reclaimed once dW_l is computed.

## Slide 26
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
26
C data structures — walkthrough
Why each field is what it is, and where it lives in memory
1
layer_t struct
Plain-old-data. A single L_NUM-long table of these describes the whole model. The runtime walks LAYERS[i] in order; no dynamic dispatch, no virtual calls.
2
W pointer
Points into either Flash (W0) or SRAM (W_ram), depending on whether the layer is being trained. The exporter writes both copies; boot code memcpy's into SRAM.
3
M packed bitmap
ceil(N/8) bytes per layer. A 10×100 Linear has 1000 bits = 125 bytes — versus a sparse-CSR encoding which would need int16 indices and ~12× more memory for a 90% sparse layer of this size.
4
s_w, s_a_in, s_a_out
Three fp32 scalars per layer. Negligible memory cost (~3 KB for the whole model) and they're cache-friendly because they live next to the layer descriptor.
5
kind tag
Selects which kernel to dispatch — Conv2d, Linear, or DepthwiseConv. The forward and backward switch on this tag once per layer, not once per MAC.
6
Runtime SRAM mirrors
W_ram, M_ram and dW_ram are sized to TOTAL_W / TOTAL_M_BYTES at link time. A_ram is double-buffered so layer l's output overwrites layer l-1's input.

## Slide 27
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
27
C — int8 kernels
Forward reuses CMSIS-NN; backward is custom int8 GEMM
// Mask-aware forward (Linear)
void qfc_forward_masked(const layer_t *L,
const int8_t *x_in, int8_t *y_out) {
for (int o = 0; o < L->fan_out; ++o) {
int32_t acc = 0;
for (int i = 0; i < L->fan_in; ++i) {
int idx = o * L->fan_in + i;
if (!bit_get(L->M, idx)) continue; // sparse skip
acc += (int32_t)x_in[i] *
(int32_t)L->W[idx];
}
float yf = acc * (L->s_w * L->s_a_in);
y_out[o] = sat_int8(roundf(yf / L->s_a_out));
}
}
// Backward -- dW and dX in int8
void qfc_backward(const layer_t *L,
const int8_t *x_in, // forward input
const int8_t *dy, // upstream grad
int8_t *dW_out, int8_t *dx_out) {
// dW = x^T . dy (mask applied)
for (int o = 0; o < L->fan_out; ++o)
for (int i = 0; i < L->fan_in; ++i) {
int idx = o * L->fan_in + i;
if (!bit_get(L->M, idx)) {
dW_out[idx] = 0; continue; }
int32_t a = (int32_t)x_in[i] *
(int32_t)dy[o];
dW_out[idx] = sat_int8(roundf(
a * L->s_a_in / L->s_w));
}
// dx = dy . W^T (analogous loop)
}

## Slide 28
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
28
C int8 kernels — walkthrough
What the forward and backward kernels actually do, MAC by MAC
1
Outer loop = output neurons
qfc_forward_masked walks one output neuron at a time. acc is int32 to avoid overflow during MAC accumulation across fan_in input weights.
2
Sparse skip via bit_get
Before each MAC, check the mask bit. If zero, continue — that single branch makes the kernel actually sparse-fast, not just sparse-correct.
3
Rescale & saturate
After accumulation, multiply by (s_w · s_a_in), divide by s_a_out, round to nearest, saturate to int8. Same int8-output rescaling as CMSIS-NN.
4
Backward dW kernel
dW[o,i] = x_in[i] · dy[o] — the outer-product form. The mask check zeros gradient entries for inactive weights, so dW slots that won't be applied don't even get a write.
5
Scale arithmetic in backward
The fp scale on the accumulated int32 is (s_a_in · s_g_out / s_w). The runtime stores all three so the kernel only does one float multiply and one float divide per output.
6
Backward dx kernel
dx[i] = sum_o dy[o] · W[o,i] — same structure as the forward but with dy and W transposed. Mask-aware: skip if the corresponding W slot is masked out.

## Slide 29
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
29
C — partial update & mask update
FQT top-k SGD and RigL prune-and-grow, both running on the MCU
// FQT partial update -- bounded min-heap
void fqt_partial_update(layer_t *L,
const int8_t *dW, float eta, int k) {
heap_t H; heap_init(&H, k); // min-heap |dW|
int N = L->fan_in * L->fan_out;
for (int i = 0; i < N; ++i) {
if (!bit_get(L->M, i)) continue;
heap_push(&H, i, abs8(dW[i])); // O(log k)
}
for (int j = 0; j < H.size; ++j) {
int idx = H.idx[j];
int32_t step = (int32_t)roundf(
eta * dW[idx] *
(L->s_w / L->s_a_in));
L->W[idx] = sat_int8(
(int32_t)L->W[idx] - step);
}
}
// RigL mask update on the MCU (every dT)
void rigl_update(layer_t *L,
const int8_t *g_dense, float drop_frac) {
int active = popcount_bits(L->M, BITS_OF(L));
int k = (int)(drop_frac * active);
// 1) drop : k smallest |W| over active
heap_t Hd; heap_init(&Hd, k); // max on |W|
for (int i = 0; i < N(L); ++i)
if (bit_get(L->M, i))
heap_push_max(&Hd, i, abs8(L->W[i]));
for (int j = 0; j < Hd.size; ++j)
bit_clr(L->M, Hd.idx[j]);
// 2) grow : k largest |g_dense| over inactive
heap_t Hg; heap_init(&Hg, k); // min on |g|
for (int i = 0; i < N(L); ++i)
if (!bit_get(L->M, i))
heap_push_min(&Hg, i, abs8(g_dense[i]));
for (int j = 0; j < Hg.size; ++j) {
bit_set(L->M, Hg.idx[j]);
L->W[Hg.idx[j]] = 0; // zero-init
}
}

## Slide 30
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
30
C update kernels — walkthrough
FQT top-k SGD and RigL drop-and-grow on the MCU
1
Bounded min-heap (FQT)
k = κ·|active|, typically ~10% of the weights. A min-heap of size k keeps memory bounded — we never materialise the full sorted list, just the running top-k.
2
Skip masked slots
Inside the loop, bit_get(L->M, i) gates whether the weight is considered at all. The heap only ever contains active-mask indices, by construction.
3
Scaled int8 step
step = round(η · dW · (s_w / s_a_in)) — a single int32, then saturate-subtract from int8 W. All in-place; no temporary dense tensor.
4
popcount for active count
popcount_bits over the mask bitmap returns |active| in a single pass — required to compute k. CMSIS provides __RBIT/__CLZ helpers that turn this into a few cycles per byte.
5
Drop heap (RigL, max-heap on |W|)
Two passes: build a max-heap of |W| over active slots, then pop the k smallest. bit_clr flips their mask bits to inactive. W values stay untouched — they'll be overwritten by grow.
6
Grow heap (RigL, min-heap on |g|)
Build a min-heap of |g_dense| over inactive slots; pop the k largest. bit_set the mask, then L->W[idx] = 0 — fresh zero start, no carryover from whatever was there before.

## Slide 31
MCU Implementation
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
31
C — memory budget & deployment
Fitting a trainable model into 320 KB of SRAM on the F746ZG
SRAM budget — 320 KB
W + masks (int8)
90 KB
dW gradient buffer
60 KB
Activations (A0/A1)
80 KB
Heaps + scratch
30 KB
Stack + system
60 KB
Total: 320 KB · zero headroom — every byte is budgeted.
Deployment steps
1
Flash init weights + header to F746ZG via ST-Link.
2
USB-VCP serial channel for batch streaming and log retrieval.
3
DWT cycle counter on the M7 → per-step latency in µs.
4
External INA-219 on the 3.3 V rail → energy per epoch.
5
Bit-exact validation against PyTorch (same RNG seed).
Numbers to report in the thesis
• Speaker-ID accuracy — vs. each of the 4 conditions
• Per-step latency — ms / training step on F746ZG
• Peak SRAM use — snapshot at backward / mask update
• Energy per epoch — mJ, from INA-219
• Weight memory — KB on disk (sparse-stored int8)

## Slide 32
Implementation Roadmap
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
32
Build order — milestones M1 → M11
Validate at every step; never combine two unverified changes
M1
FP32 dense baseline
Train an unmodified Conv/Linear stack on the 40-speaker split. Locks the data pipeline, model topology, and the loss curve to beat.
Gate: ≥ 85% test accuracy.
M2
Fake-quant + STE forward
Swap Linear/Conv for QLinear/QConv with QuantSTE but still backprop in fp32. Forward sees int8-valued tensors.
Gate: ≤ 1% accuracy drop vs. M1.
M3
Real int8 forward kernels
Replace the fake-quant matmul with an integer matmul returning int32 accumulators. Same loss curve as M2 within rounding.
Gate: bit-comparable outputs.
M4
Int8 backward + partial update
Add hand-coded int8 dW / dA kernels and the top-κ gradient filter. This is condition B (FQT dense).
Gate: ≤ 2% accuracy drop vs. M1.
M5
FP32 RigL manager
Build the mask manager; sparsify the M1 model and retrain. This is condition C (FP32 + RigL).
Gate: ≤ 2% accuracy at 90% sparsity.
M6
FQT × RigL combined
Hook the RigL manager into the M4 loop. This is condition D — the thesis claim.
Gate: ≤ 4% drop vs. M1, all in int8.
M7
Exporter + replay test
Dump weights_q8.c, scales.c, mask_bitmap.c. Replay test consumes the dump and reproduces M6 byte-for-byte.
Gate: 100% byte match first N steps.
M8
MCU forward path
Port arm_*_s8 forward + mask-aware skip onto the F746ZG. Compare logits with Python on the exported model.
Gate: max |Δlogit| ≤ 1 LSB.
M9
MCU int8 backward
Hand-write qfc_backward / qconv_backward. Match Python dW byte-for-byte for the first 10 steps.
Gate: bit-exact dW for 10 batches.
M10
MCU FQT partial update
Bounded min-heap + in-place saturating subtract. Full epoch on-device; record latency, peak SRAM, energy.
Gate: accuracy curve = Python M4.
M11
MCU RigL mask update
Drop+grow heaps on-device. Run the full M6 schedule on the F746ZG; collect all four conditions' on-device numbers.
Gate: thesis deliverable — final table.
Rule
Never advance to the next milestone with two changes outstanding — regressions become un-bisectable.

## Slide 33
Experimental Plan
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
33
Three-phase experimental plan
From PyTorch baselines to a working int8 sparse trainer on the F746ZG
Phase 1
PyTorch baselines
Build all four conditions on the workstation. Lock data splits and the seed; collect accuracy, weight memory, FLOPs, wall-clock. Demonstrate that FQT+RigL is competitive with FP32 dense in simulation.
Phase 2
GPU-level integration
Tighten quantization scales, calibrate kappa (FQT top-k) and (α, T_end, ΔT) for RigL on this dataset. Profile the dense-backward step RigL needs and confirm it stays affordable when quantized.
Phase 3
MCU port
Port the validated configuration to the F746ZG. Hand-write the int8 backward and heaps; reuse CMSIS-NN for the forward. Measure latency, peak SRAM, and energy. Achieve bit-exact agreement with the Python run for N steps.

## Slide 34
Conclusion
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
34
Summary
Where the contribution sits and what makes it novel
The thesis claim
FQT compresses every operation; RigL compresses the operand. Their intersection is the open question this thesis answers — and the implementation path runs from a PyTorch prototype directly to int8 sparse-from-scratch training on the STM32 Nucleo-F746ZG, evaluated on a closed-set LibriSpeech speaker-identification task.
Memory
Sparse storage + int8 collapses both weights and activations. Dense FP32 baselines simply do not fit in 320 KB SRAM.
Compute
Top-κ FQT gradients × RigL mask leave only a small active set to update each step — the backward pass is doubly sparse.
Topology
Mask grows toward the connections that matter most, even though it is scored from int8 gradients — the open question.
Deployment
End-to-end demonstration on real hardware, not a simulation paper — latency, SRAM, and energy reported.

## Slide 35
References
UDE
UNIVERSITÄT
DUISBURG · ESSEN
Offen im Denken
www.uni-due.de
12.05.2026
35
Key references
The papers and toolchains this thesis builds on
Deutel et al., 2024
On-Device Training of Fully Quantized DNNs on Cortex-M Microcontrollers — int8 forward + backward + update with dynamic partial-gradient SGD.
Evci et al., 2020
Rigging the Lottery: Making All Tickets Winners — sparse-from-scratch dynamic mask training (RigL) with magnitude-prune + gradient-grow.
Hoefler et al., 2021
Sparsity in Deep Learning — taxonomy and background for the sparse-training literature; useful for situating RigL among alternatives.
Panayotov et al., 2015
LibriSpeech: an ASR corpus based on public domain audio books — the dataset used here for closed-set speaker identification (dev-clean, 40 speakers).
ARM, 2018+
CMSIS-NN — int8 neural-network kernels for Cortex-M; basis for the forward path on the F746ZG.