## Slide 1
MASTER'S THESIS · REVISED SCOPE · PURE C
Fully Quantized Training meets RigL
Sparse-from-scratch int8 training on a Cortex-M7 — implemented in pure C
11
milestones · C1 → C11
0
lines of Python
320 KB
SRAM target · F746ZG
Mohamed Elshorbagy · Universität Duisburg-Essen · May 2026

## Slide 2
SCOPE · CHANGE NOTICE
What changed from the original presentation
Decision made 2026-05-19 — supersedes the Python prototype plan
What the original deck said
• Stage A — Python prototype in PyTorch (slides 15–23)
• Stage B — C port to F746ZG (slides 24–31)
• M1–M11 build order: 7 Python milestones, 4 MCU milestones
• Four-condition comparison treated as the experimental backbone:
FP32 dense / FQT dense / FP32 + RigL / FQT + RigL
• PyTorch acted as the reference for bit-exact validation on the MCU
What the revised plan says
• Pure C from scratch — no PyTorch anywhere
• Stage A — host-PC C kernels and data pipeline (C1–C7)
• Stage B — MCU port to F746ZG (C8–C11)
• Four-condition comparison DROPPED — without an FP32 reference,
we report only on-device sparse-int8 results
• Validation strategy becomes hand-built golden tests at every kernel
• Deliverable: end-to-end FQT+RigL training run on the F746ZG
Tradeoff accepted: weaker experimental comparison in exchange for a single-language codebase and direct path to the target hardware.
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
2 / 16

## Slide 3
ROADMAP · REVISED
Build order — C1 → C11
Stage A: host PC validates the design. Stage B: port to F746ZG.
Stage A — Host PC (C1 → C7)
Stage B — MCU F746ZG (C8 → C11)
C1
Build system + golden int8 MAC test
C2
int8 Linear + Conv2d forward kernels
C3
int8 backward kernels (dW, dA)
C4
SGD with momentum + FQT partial update
C5
RigL mask manager (ER-K, prune-and-grow)
C6
MFCC + audio pipeline (host PC)
C7
End-to-end training run on host C
C8
MCU project skeleton + forward port
C9
MCU int8 backward
C10
MCU FQT partial + RigL mask update
C11
End-to-end MCU training run (deliverable)
Discipline rule — never advance to the next milestone with two changes outstanding; regressions become un-bisectable.
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
3 / 16

## Slide 4
C1 · HOST PC
Build system + golden int8 MAC test
Goal: smallest possible C program that proves the toolchain is alive.
Purpose
Lock down the C toolchain and validate that an int8 multiply-accumulate behaves exactly as expected. This is the smallest verifiable unit on which every later kernel depends. Without a known-good build environment and a known-good MAC, every downstream bug is ambiguous between 'algorithm wrong' and 'compiler/toolchain wrong'.
How to start
1. Install a C11 toolchain (MSYS2 + gcc on Windows, or WSL2 + gcc).
2. Create a single-file project mac_test.c. No Makefile yet.
3. Compile: gcc -O2 -Wall -Wextra -std=c11 -o mac_test mac_test.c
4. Run and confirm the program prints 'MAC = 4' and exits with code 0.
5. Verify int32_t accumulator, both operands cast to int32 BEFORE multiply.
GATE
mac_test exits with code 0 on the hand-built example · no floating point yet.
Algorithm
ALGORITHM golden_mac_test
INPUTS : x[N] (int8 array)
w[N] (int8 array)
N (length)
OUTPUT : acc (int32)
---------------------------------------------------
1. acc <- 0
2. for i = 0 .. N-1:
3. acc <- acc + (int32) x[i] * (int32) w[i]
4. return acc
HAND-COMPUTED REFERENCE
x = [ 10, -5, 20, 3]
w = [ 2, 4, -1, 8]
acc = 10*2 + (-5)*4 + 20*(-1) + 3*8
= 20 + (-20) + (-20) + 24
= 4
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
4 / 16

## Slide 5
C2 · HOST PC
int8 Linear + Conv2d forward kernels (mask-aware)
Goal: sparse-quantized forward layer kernels validated on host PC.
Purpose
Implement the two forward primitives needed by the model: a mask-aware int8 Linear and a mask-aware int8 Conv2d. The mask check must be a real branch — skipping masked weights is what turns RigL sparsity into a speedup later. Per-layer scales (s_w, s_a_in, s_a_out) enter here for the first time.
How to start
1. Define layer_t struct + bit_get / bit_set / bit_clr inline helpers.
2. Build a golden test: 4-in / 3-out Linear with hand-picked weights and mask.
3. Compute the expected output by hand. Save as expected[3] in a header.
4. Run the kernel, assert byte-for-byte equality.
5. Repeat with a tiny 1x1x4x4 -> 2x1x4x4 Conv2d golden.
GATE
Linear & Conv2d kernels match hand-built golden outputs byte-for-byte.
Algorithm
ALGORITHM linear_forward_masked
INPUTS : L (W, M_bitmap, s_w, s_a_in, s_a_out,
fan_in, fan_out)
x_in[fan_in] (int8)
OUTPUT : y_out[fan_out] (int8)
---------------------------------------------------
1. scale <- s_w * s_a_in / s_a_out
2. for o = 0 .. fan_out-1:
3. acc <- 0 // int32
4. for i = 0 .. fan_in-1:
5. idx <- o*fan_in + i
6. if bit_get(M, idx) == 1:
7. acc <- acc +
(int32)x_in[i] *
(int32)W[idx]
8. y_out[o] <- sat_int8( round( acc * scale ) )
ALGORITHM conv2d_forward_masked (NCHW, stride=1, pad=1)
outer: for each (oc, oh, ow) ...
acc <- 0
for ic, kh, kw:
idx <- weight_index(oc, ic, kh, kw)
if bit_get(M, idx):
acc += x[ic, oh+kh, ow+kw] * W[idx]
y[oc, oh, ow] <- sat_int8( round(acc * scale) )
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
5 / 16

## Slide 6
C3 · HOST PC
int8 backward kernels — dW and dA
Goal: hand-coded int8 gradients for Linear and Conv2d.
Purpose
Backward is the place where there is no external library to lean on. We compute dW (the weight gradient) and dA (the gradient w.r.t. the layer input) in int8 with their own scale s_g. The mask gates which dW entries are even worth writing — masked slots get zero and skip the heavy work.
How to start
1. Write the dW kernel first — it is the simpler outer product.
2. Verify dW against a numerical finite-difference check on a tiny network.
3. Add the dx kernel; verify by composing with a forward pass.
4. Same pattern for Conv2d: dW = correlation(x, dy), dx = full-conv(dy, W^T).
5. Keep mask checks explicit — they are not optional for sparse training.
GATE
dW agrees with finite-difference within 1 LSB · full backward chain rule verified.
Algorithm
ALGORITHM linear_backward
INPUTS : L, x_in[fan_in], dy[fan_out] (int8)
OUTPUT : dW[fan_in*fan_out], dx[fan_in] (int8)
---------------------------------------------------
// dW = x_in^T outer dy (mask applied)
1. for o = 0 .. fan_out-1:
2. for i = 0 .. fan_in-1:
3. idx <- o*fan_in + i
4. if NOT bit_get(M, idx):
5. dW[idx] <- 0; continue
6. a <- (int32)x_in[i] * (int32)dy[o]
7. dW[idx] <- sat_int8( round( a *
s_a_in * s_g_out / s_w ) )
// dx = dy . W^T (mask applied)
8. for i = 0 .. fan_in-1:
9. acc <- 0
10. for o = 0 .. fan_out-1:
11. idx <- o*fan_in + i
12. if bit_get(M, idx):
13. acc += (int32)dy[o] * (int32)W[idx]
14. dx[i] <- sat_int8( round( acc *
s_w * s_g_out / s_g_in ) )
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
6 / 16

## Slide 7
C4 · HOST PC
SGD with momentum + FQT partial update
Goal: integer-step optimizer that updates only top-k gradients.
Purpose
FQT's headline ~49% latency win comes from writing only the top-k weights per step, not all of them. We implement SGD-with-momentum in integer steps and a bounded min-heap that selects the kappa * |active| largest |dW| entries per layer. Updates are in-place against the int8 W tensor.
How to start
1. Implement a bounded min-heap (parent/child arithmetic) — ~50 lines of C.
2. Unit-test the heap on random inputs against qsort's top-k.
3. Wire the heap into fqt_partial_update; test on a known dW.
4. Add momentum as an int8 velocity buffer per layer.
5. Set kappa=1.0 first to debug, then drop to 0.1 (Deutel's value).
GATE
On a static dW input, partial update modifies exactly k weights and matches a brute-force top-k reference.
Algorithm
ALGORITHM fqt_partial_update
INPUTS : L (W, M, s_w, s_a_in), dW[N],
eta (lr), kappa (top-k fraction)
OUTPUT : W mutated in place
---------------------------------------------------
1. active <- popcount_bits(L.M)
2. k <- floor(kappa * active)
3. heap_init(H, capacity=k) // min-heap on |dW|
4. for i = 0 .. N-1:
5. if bit_get(L.M, i):
6. heap_push(H, idx=i, key=|dW[i]|)
// pops smaller when full
7. // H now holds the k indices with the largest |dW|
8. for j = 0 .. H.size-1:
9. idx <- H.idx[j]
10. step <- round( eta * dW[idx] * s_w / s_a_in )
11. W[idx] <- sat_int8( (int32)W[idx] - step )
MOMENTUM (per-layer int8 velocity buffer V[N]):
V[idx] <- sat_int8( mu * V[idx] + dW[idx] )
use V in place of dW at line 10
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
7 / 16

## Slide 8
C5 · HOST PC
RigL mask manager — ER-K init, cosine drop, prune-and-grow
Goal: dynamic sparse mask that evolves during training.
Purpose
RigL is what turns a static-sparsity model into one that finds its own topology. The mask manager owns ER-K initialization (denser big layers, sparser small ones), a cosine schedule for the drop fraction, and a two-heap drop-and-grow operation every dT iterations until t_end.
How to start
1. Implement ER-K init: density per layer + random bit pattern + W *= M.
2. Cosine schedule as a single math function: f_t.
3. Reuse the bounded heap from C4 for drop and grow with min/max variants.
4. Test on a 2-layer model — print active count before/after a refresh.
5. Verify |drop| == |grow| so sparsity stays exact.
GATE
Mask churn equals planned k each refresh, sparsity stays constant, new W slots are exactly zero.
Algorithm
ALGORITHM rigl_update (called when t mod dT == 0, t < T_end)
INPUTS : L, g_dense[N], drop_frac
OUTPUT : L.M and L.W mutated
---------------------------------------------------
1. active <- popcount_bits(L.M)
2. k <- floor(drop_frac * active)
// ----- DROP: k smallest |W| over active slots -----
3. heap_init(Hd, capacity=k) // max-heap on |W|
4. for i in 0..N:
5. if bit_get(L.M, i):
6. heap_push_max(Hd, i, |W[i]|)
7. for j in 0..Hd.size: bit_clr(L.M, Hd.idx[j])
// ----- GROW: k largest |g_dense| over INACTIVE slots -----
8. heap_init(Hg, capacity=k) // min-heap on |g|
9. for i in 0..N:
10. if NOT bit_get(L.M, i):
11. heap_push_min(Hg, i, |g_dense[i]|)
12. for j in 0..Hg.size:
13. bit_set(L.M, Hg.idx[j])
14. L.W[Hg.idx[j]] <- 0 // zero-init grown slots
DROP-FRACTION SCHEDULE
f(t) = (alpha/2) * (1 + cos(pi * t / T_end))
ER-K INIT (per layer): density = (1-s) * N / max(fan_in, fan_out)
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
8 / 16

## Slide 9
C6 · HOST PC
MFCC + audio pipeline
Goal: .flac files in, (1,13,101) int8 MFCC tensors out.
Purpose
Without PyTorch / torchaudio we own the entire feature pipeline. Decode .flac to PCM (dr_flac single-header library), compute 13 MFCCs at 25ms / 10ms hop with a 40-mel filterbank, quantize to int8 with a fixed scale, and cache to disk so re-runs are I/O-bound instead of FFT-bound.
How to start
1. Pull dr_flac.h and kissfft (single-file C, no build system needed).
2. Implement mel-filterbank by hand — ~30 lines of triangular weights.
3. Validate one MFCC frame against a reference (Python librosa one-time check).
4. Iterate over the 40-speaker LibriSpeech subset, write .f8 cache files.
5. Sanity check: feat file size ~ 13*101 bytes + scale per utterance.
GATE
One MFCC frame matches librosa within rounding · full dataset cached on disk.
Algorithm
ALGORITHM mfcc_extract
INPUTS : pcm[SR] (1 second, 16 kHz), n_mfcc=13,
n_mels=40, win=400, hop=160, n_fft=400
OUTPUT : feat[1][13][101] (int8)
---------------------------------------------------
1. pad-or-truncate(pcm, SR)
2. pre-emphasis: pcm[i] -= 0.97 * pcm[i-1]
3. for each frame f in [0..100]:
4. seg <- pcm[f*hop : f*hop+win] * hamming_window
5. spec <- |FFT(seg, n_fft)|^2 // power spectrum
6. mel <- mel_filterbank(spec, 40) // 40 bins
7. log_mel <- log(mel + 1e-6)
8. cep[f] <- DCT(log_mel)[0:13] // 13 cepstra
9. scale <- max(|cep|) / 127
10. feat <- round(cep / scale) saturated to int8
11. write feat + scale to <utt_id>.f8
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
9 / 16

## Slide 10
C7 · HOST PC
End-to-end training run — sparse int8 FQT+RigL converges
Goal: prove the algorithm works on real data BEFORE touching the MCU.
Purpose
Wire C2–C6 together into one training program. Loads the cached MFCC tensors, runs the sparse-int8 forward, the int8 backward, the FQT partial update, and the periodic RigL mask refresh. Trains a small Conv→Conv→Linear→Linear stack on the 40-speaker split. This is the moment the thesis algorithm becomes real.
How to start
1. Choose model topology that fits 320 KB SRAM at 90% sparsity (4 layers).
2. Run for 1 epoch first — confirm loss decreases. Treat as smoke test.
3. Then run the full schedule, log per-epoch val accuracy.
4. Tune kappa and dT if convergence stalls; document choices.
5. Save final int8 weights + bitmask + scales as binary files for C8.
GATE
Test accuracy stabilises (target ~70–85%) · weights export cleanly for the MCU port.
Algorithm
ALGORITHM train_e2e
INPUTS : cached MFCC dataset, model layers L[0..3],
sparsity=0.9, kappa=0.1, T_end, dT, eta, epochs
OUTPUT : trained int8 weights, accuracy curve
---------------------------------------------------
1. rigl_erk_init(layers, sparsity=0.9)
2. for epoch in 1..epochs:
3. shuffle train_set
4. for (x, y) in train_set:
5. // ---- sparse forward + loss
6. logits <- model_forward(layers, x)
7. dL_dlogits <- softmax_xent_grad(logits, y)
8. // ---- sparse backward
9. dW[*], dA[*] <- model_backward(layers, dL_dlogits)
10. // ---- FQT partial update (active set only)
11. for L in layers: fqt_partial_update(L, dW[L])
12. // ---- RigL mask refresh
13. if t mod dT == 0 and t < T_end:
14. g_dense <- model_backward_dense(layers, dL_dlogits)
15. f_t <- (alpha/2)(1 + cos(pi t/T_end))
16. for L: rigl_update(L, g_dense[L], f_t)
17. t <- t + 1
18. acc_val <- evaluate(layers, val_set)
19. log(epoch, acc_val); save_checkpoint_if_best()
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
10 / 16

## Slide 11
C8 · MCU F746ZG
Project skeleton + forward port
Goal: same forward kernels running on the F746ZG, bit-exact vs host C.
Purpose
First contact with the target hardware. Bring up an STM32CubeIDE project, wire USART3 for printf, enable the DWT cycle counter, and port the C2 forward kernels onto the MCU. CMSIS-NN handles standard kernels — we only need the mask-aware wrapper around its int8 GEMM.
How to start
1. Get printf('hello\n') over USART3 at 115200 baud working first.
2. Verify DWT cycle counter ticks (~216M per second).
3. Port qfc_forward_masked unchanged; only the SRAM mirrors differ.
4. Stream a fixed input batch from host via UART; collect logits back.
5. Diff against host-C output — must match within 1 LSB.
GATE
max |delta_logit| <= 1 LSB versus host-C reference · DWT reports per-step latency.
Algorithm
ALGORITHM mcu_forward_bringup
STEPS
---------------------------------------------------
1. CubeMX: enable USART3, FPU, 216 MHz clock.
2. Pull CMSIS-NN as submodule; add to include path.
3. In main():
CoreDebug->DEMCR |= TRCENA_Msk;
DWT->CYCCNT = 0;
DWT->CTRL |= CYCCNTENA_Msk;
4. Flash weights_q8.c + masks.c + scales.c
(binary blobs exported from C7) as const arrays.
5. Boot: memcpy(W_ram, W0, TOTAL_W)
memcpy(M_ram, M0, TOTAL_M_BYTES)
6. Implement model_forward(x, logits):
for l in 0..L-1:
switch LAYERS[l].kind:
LINEAR : qfc_forward_masked(...)
CONV2D : qconv2d_forward_masked(...)
swap input/output buffers (A_ram ping-pong)
7. Send one fixed input over UART, run model_forward,
UART back the int8 logits.
8. Diff against host-C reference on the same input.
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
11 / 16

## Slide 12
C9 · MCU F746ZG
int8 backward on the MCU
Goal: backward kernels running on-device, dW bit-identical to host C.
Purpose
Port the C3 backward kernels (dW, dA for Linear and Conv2d) onto the F746ZG. This is the heaviest C work in the project — CMSIS-NN does not ship backward kernels, so we own this code. Validation is brutal: dW must match the host-C reference byte-for-byte for the first 10 mini-batches.
How to start
1. Port qfc_backward unchanged from host C — the algorithm is the same.
2. Make qconv_backward stride/pad/dilation match host C exactly.
3. Stream one fixed batch from host, run forward + backward, UART back dW.
4. Diff each layer's dW against host-C reference for 10 batches.
5. Profile peak SRAM use — must not exceed memory map budget.
GATE
dW byte-identical to host C for 10 batches · peak SRAM within 320 KB.
Algorithm
ALGORITHM mcu_backward_step
---------------------------------------------------
1. forward pass (C8) leaves A_l in SRAM ping-pong.
2. dA_L <- softmax_xent_grad(logits, y) (int8)
3. for l = L-1 .. 0:
4. switch LAYERS[l].kind:
5. LINEAR :
qfc_backward(L,
x_in = A_{l-1},
dy = dA_{l},
dW_out = dW_ram_l,
dx_out = dA_{l-1})
6. CONV2D :
qconv_backward(L, ...)
7. reuse A_{l-1} buffer once dW_l is written
MEMORY DISCIPLINE
- dW gradient buffer is shared across layers, one at a time
- A_ram pages are reclaimed in reverse-layer order
- peak SRAM use is at the deepest layer's backward step
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
12 / 16

## Slide 13
C10 · MCU F746ZG
FQT partial update + RigL mask update on-device
Goal: full training step on-device (forward + backward + update + mask).
Purpose
Bring the FQT top-k heap and the RigL drop-and-grow heaps to the MCU. Both use bounded heaps so memory stays predictable. After this milestone the F746ZG can take one full training step end-to-end: forward, backward, partial update, and (every dT steps) a mask refresh.
How to start
1. Port the bounded heap from C4/C5 as static memory (no malloc on MCU).
2. Verify mask churn matches host C on a 100-step run.
3. Read DWT before/after each phase — log latencies separately.
4. Confirm peak SRAM at refresh step (worst case) stays within budget.
5. Trigger one RigL refresh from a known seed, byte-match mask vs host.
GATE
100-step on-device run reproduces host-C loss curve · mask churn byte-matches host.
Algorithm
ALGORITHM mcu_training_step (one minibatch)
---------------------------------------------------
1. receive (x_int8, y) over UART
2. model_forward(x, logits) // C8
3. dA_L = softmax_xent_grad(logits, y)
4. model_backward(dA_L) // C9
// ----- FQT partial update per layer ---------------
5. for L in layers:
6. fqt_partial_update(L, dW_ram_l, eta, kappa)
// bounded min-heap, ~10% of weights updated
// ----- RigL refresh every dT steps -----------------
7. if t mod dT == 0 and t < T_end:
8. model_backward_dense(dA_L) // no mask
// produces g_dense for inactive slots only
9. f_t = (alpha/2)*(1+cos(pi*t/T_end))
10. for L: rigl_update(L, g_dense_l, f_t)
// drop smallest |W| in active set
// grow largest |g| in inactive set
11. t <- t + 1
12. UART back: loss, |active|, latency_cycles
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
13 / 16

## Slide 14
C11 · MCU F746ZG
End-to-end MCU training run — thesis deliverable
Goal: full training schedule on the F746ZG, produce the result table.
Purpose
Run the full training schedule from C7 on the F746ZG. Stream the cached MFCC dataset over UART, log latency / loss / accuracy per step, capture energy from an external INA-219 on the 3.3V rail. This is the deliverable the thesis reports.
How to start
1. Wire INA-219 (I2C) to the host PC and the 3.3V VDD rail.
2. Stream MFCC features from host over UART (or USB-VCP at higher rate).
3. Run a short schedule first (~500 steps) to verify pipeline.
4. Then run the full schedule overnight; let logs accumulate.
5. Produce the final table for the thesis writeup.
GATE
Full schedule completes on-device · accuracy + latency + SRAM + energy table produced.
Algorithm
ALGORITHM mcu_training_run
INPUTS : cached MFCC dataset (streamed from host),
schedule (epochs, dT, T_end, eta, kappa, alpha)
OUTPUT : on-device accuracy + latency + memory + energy table
---------------------------------------------------
1. init INA-219 sampling at 1 kHz on the host side
2. for epoch in 1..N:
3. for (x, y) in stream(train_set):
4. mcu_training_step(x, y) // C10
5. host logs: cycles, loss, |active|
6. UART batch over val_set:
7. forward only, host logs accuracy
8. host logs: peak SRAM (from MCU snapshot),
mJ per epoch (INA-219 integration)
9. write final table:
accuracy_test · latency_per_step · peak_SRAM
· energy_per_epoch · final_weights
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
14 / 16

## Slide 15
DELIVERABLE · WHAT GETS REPORTED
Final outputs of the revised pure-C plan
What ends up in the thesis writeup, given the dropped four-condition comparison.
Speaker-ID accuracy
Test-set accuracy of the trained sparse-int8 model on the 40-speaker LibriSpeech split, measured on-device.
Per-step latency
Milliseconds per training step on the F746ZG, broken down: forward, backward, FQT update, RigL refresh.
Peak SRAM use
Snapshot at the backward / mask-update step. Must stay within the 320 KB budget; report headroom.
Energy per epoch
Millijoules from the external INA-219 sampling the 3.3V rail. The number a real edge deployment cares about.
Sparse weight memory
KB of int8 weights + bitmap on disk after training. Demonstrates the model fits in 1 MB Flash.
Master's Thesis · FQT + RigL · Pure-C revision · May 2026
16 / 16