## Slide 1
On-Device Training
Combining Fully Quantized Training & RigL Sparse Learning
for Embedded Speaker Identification
Target Hardware: STM32 Nucleo-F746ZG (Cortex-M7, 320 KB SRAM) Dataset: LibriSpeech — Closed-Set Speaker ID Implementation: Pure C · No Python · No PyTorch
Master's Thesis · Mohamed · 2026

## Slide 2
Agenda
01
Motivation & Problem Statement
02
Key Research: FQT, RigL, and Sparsity
03
Target Hardware & Application
04
Scope Decision: Why Pure C?
05
Framework Architecture
06
Implementation: Modules Built
07
Experiment: MNIST Validation
08
Remaining Work & Roadmap
09
Expected Results & Contributions

## Slide 3
Motivation — Why On-Device Training?
📵 No Cloud Dependency
Microcontrollers in remote or privacy-sensitive deployments cannot rely on constant network access to a cloud training server.
🔒 Privacy & Security
Speaker biometric data must never leave the device. Local training eliminates data exfiltration risk entirely.
⚡ Real-Time Adaptation
Models that learn continuously on the device can adapt to new users, acoustic environments, and drifting sensor characteristics.
🔋 Extreme Resource Constraints
MCUs have 100–512 KB SRAM and run at 10–216 MHz. State-of-the-art training frameworks are 3–4 orders of magnitude too heavy.

## Slide 4
The Research Gap
What Already Exists
✓ Inference-only TinyML (TFLite Micro, CMSIS-NN) ✓ Float32 on-device training (backprop on M4/M7) ✓ Fully Quantized Training — int8 forward + backward (Deutel et al., 2024) ✓ Dynamic sparse training — RigL topology updates (Evci et al., 2020) ✓ Sparsity survey & theory (Hoefler et al., 2021)
What Does NOT Exist Yet
✗ FQT + RigL combined on a microcontroller ✗ Sparse topology updates under int8 arithmetic ✗ Memory-feasible gradient accumulation for RigL in <320 KB ✗ Pure-C, zero-dependency on-device training stack ✗ End-to-end audio → MFCC → train → infer on MCU

## Slide 5
Research Question
Can RigL-style dynamic sparse training be made to work under
fully quantized training (int8 forward + backward + gradient)
on a Cortex-M7 microcontroller, for speaker identification?
int8 arithmetic
sparse topology
320 KB SRAM
no OS / no malloc
speaker ID accuracy

## Slide 6
Key Reference 1 — Fully Quantized Training (Deutel et al., 2024)
Deutel, Roth, Terwedow et al. — "On-Device Training of Fully Quantized DNNs on Cortex-M Microcontrollers" (2024)
Full int8 forward + backward pass with int32 accumulators. Dynamic partial gradient updates to cut memory.
int8 Everything
Weights, activations, gradients and optimizer state are all stored and computed in int8/int32. No float at runtime.
~35% Memory Win
Compared to float32 baseline on the same MCU. Achieved through quantization of the backward pass, not just inference.
~49% Latency Win
Integer MACs on Cortex-M DSP instructions replace float operations. Demonstrated on M0+, M4, and M7 targets.
Partial Gradient Updates
Only a subset of layers are updated per step to stay within SRAM budget — a key memory knob for the MCU regime.

## Slide 7
Key Reference 2 — RigL Dynamic Sparse Training (Evci et al., 2020)
Evci, Gale, Menick et al. — "Rigging the Lottery: Making All Tickets Winners" (NeurIPS 2020)
Train Sparse
Forward + backward through active connections only
Magnitude Prune
Remove smallest |w| connections at each update step
Gradient Grow
Activate weights with largest |∂L/∂w| — those wanting to grow
Repeat
Topology evolves during training; final sparsity is fixed
Sparse-from-Scratch:
No dense pre-training needed. Sparsity is maintained throughout the entire run, keeping memory low.
Better than Pruning:
Outperforms magnitude-pruning post-hoc. Dynamic topology finds better sparse solutions.
Memory Efficiency:
Active connections only need storage. For high sparsity (80–95%), SRAM requirements drop proportionally.
MCU Relevance:
Sparse weight matrices mean fewer multiply-accumulate ops and smaller parameter buffers — ideal for our 320 KB budget.

## Slide 8
Key Reference 3 — Sparsity in Deep Learning (Hoefler et al., 2021)
Hoefler, Alistarh, Ben-Nun et al. — "Sparsity in Deep Learning: Pruning and Growth for Efficient Inference and Training" (JMLR 2021)
▸ Taxonomy of Sparsity
Classifies unstructured, semi-structured, and structured sparsity. Unstructured gives best accuracy-at-sparsity but requires sparse math kernels.
▸ Lottery Ticket Revisited
Systematic survey of "winning tickets" — sparse subnetworks that can be trained from scratch to match dense accuracy.
▸ Growth Strategies
Gradient-based growth (as in RigL) is shown to dominate random or activation-based growth across tasks and architectures.
▸ Training vs. Inference
Sparsity during training and sparsity during inference have different hardware implications. Our work targets both simultaneously.
▸ Memory Analysis
Dense backward pass with sparse weights still requires full gradient buffer. FQT reduces this; our integration must address it explicitly.
▸ Practical Guidance
Paper provides empirical rules: 80–90% sparsity is the regime where memory wins become significant with acceptable accuracy loss.

## Slide 9
Target Hardware — STM32 Nucleo-F746ZG
Hardware Specifications
Core
ARM Cortex-M7 @ 216 MHz
SRAM
320 KB (training budget)
Flash
1 MB (model + code storage)
FPU
Double-precision FPU (not used in int8 path)
DSP
SIMD integer MAC instructions
Interface
UART / USB / ETH for debug + data loading
Same Family
As Deutel et al. (2024) — direct comparison possible
Training Constraints
No OS/malloc
Static memory allocation only. All buffers declared at compile time.
No stdlib float
log(), exp(), sqrt() in float are expensive. Must use fixed-point or int8 approximations.
Peak RAM
Activations + gradients + weight buffers must coexist within 320 KB.
No autograd
No automatic differentiation framework. Backward pass hand-coded per layer type.
No Python
Zero host dependency. Weights loaded from Flash or UART in binary format.

## Slide 10
Application — Closed-Set Speaker Identification on LibriSpeech
Raw Audio
(16 kHz WAV)
Pre-emphasis
+ Framing
MFCC
Extraction
MLP / CNN
Classifier
Speaker ID
(softmax)
Dataset Details
▸ LibriSpeech — clean read-speech corpus derived from LibriVox
▸ dev-clean split: 40 speakers, ~5.4 hrs
▸ train-clean-100 subset available for larger experiments
▸ Sampled at 16 kHz; stored as 16-bit PCM
▸ Labels: speaker identity integers (closed-set: seen speakers only)
Feature Extraction (MFCC)
▸ 25 ms windows, 10 ms hop → ~100 frames/second
▸ 40-filter Mel filterbank
▸ 13–20 MFCCs + delta + delta-delta → 39 features/frame
▸ All computed in int16 fixed-point arithmetic on-device
▸ No external DSP library — hand-written in C
Model Architecture
▸ Small MLP: MFCC vector → 64 → 32 → N_speakers
▸ ReLU activations, softmax output
▸ Sparse: 80–90% of weight connections inactive (RigL)
▸ All weights and activations quantized to int8
▸ Fits within 320 KB SRAM at target sparsity

## Slide 11
Scope Decision — Pure C, No Python (May 19, 2026)
❌ Original Plan (Dropped)
• Python prototype with PyTorch (M1–M7)
• Quantize & export to C (M8–M9)
• Port to STM32 (M10–M11)
• Four-condition comparison table:
FP32 dense / FQT dense /
FP32 RigL / FQT+RigL
• Cross-platform PyTorch baseline
as reference numbers
✓ New Plan (Current)
• Pure C from scratch — no external
frameworks at any stage
• Hand-coded tensor engine,
autograd, layers, optimizer
• int8 FQT + RigL all in C,
running directly on F746ZG
• Deliverable: working end-to-end
sparse int8 training run on-device
• Report: accuracy + latency +
memory + energy on real hardware
Why? Choosing Pure C ensures every component is understood, verifiable, and deployable without any host dependency — a stronger research contribution for the MCU community.

## Slide 12
Framework Architecture — OnDeviceTraining (C / CMake)
User API Layer
LinearApi ReluApi SoftmaxApi SgdApi TensorApi TrainingLoopApi
Core Layer
Layer Linear Conv1d Relu Softmax Optimizer SGD LossFunction CrossEntropy MSE
Tensor & Arithmetic
Tensor DTypes Quantization Matmul Add Sub Mul Div Log Sum Rounding
Data & I/O
DataLoader NPYLoader CSVHelper Serialize Deserialize RNG
Hardware Abstraction
CMakePresets (host-pc / stm32f746 targets) • devenv.nix pinned toolchain
Both targets share identical source. The CMake preset selects arm-none-eabi-gcc + STM32 HAL for MCU or the host compiler for PC.

## Slide 13
Implementation — Tensor System & Quantization
tensor_t
Core data structure. Holds a shape_t, a pointer to raw data (void*), and a quantization_t describing scale/zero-point.
shape_t
Dimensions array + orderOfDimensions for axis tracking. Supports dynamic reshape via re-pointer (no copy).
DTypes
Enum covering FLOAT32, INT8, INT16, INT32. All arithmetic dispatches through dtype checks.
DataStorage
reserveMemory() / freeReservedMemory() — a static arena allocator. No heap malloc anywhere.
Quantization
Per-tensor scale + zero-point in float32 (stored off-device or in Flash). int8 ↔ float32 conversion helpers.
TensorConversion
tensorToFloat(), tensorToInt8(), tensorToInt32() with proper rounding and clamping.
Matmul.c
int8 × int8 → int32 with accumulation. Core of the linear layer forward pass.
Rounding.c
round_half_up(), stochastic rounding variants needed for FQT backward pass numerical stability.
Distributions.c
XAVIER_UNIFORM, ZEROS initialization. Used at model construction; avoids needing rand() at test time.
Arithmetic ops
Add, Sub, Mul, Div, Log, Sum, MinMax, Square, Comparison — all dtype-aware, statically allocated.

## Slide 14
Implementation — Layer System & Optimizer
Linear (Fully Connected)
src/layer/Linear.c
Fwd: output = W·x + b (int8×int8→int32, requantize to int8)
Bwd: ∂L/∂W = δ·xᵀ, ∂L/∂x = Wᵀ·δ (all int8, gradients in int32 accumulator)
Note: Stores weight, bias, weight_grad, bias_grad as parameter_t pairs
ReLU
src/layer/Relu.c
Fwd: max(0, x) — zero cost in int8 (compare to zero-point)
Bwd: mask where x > 0 applied to upstream delta
Note: Stateless — no parameters
Softmax
src/layer/Softmax.c
Fwd: exp(xᵢ)/Σexp(xⱼ) — uses Log.c for int8-safe approximation
Bwd: Jacobian-vector product; combined with cross-entropy for numerical stability
Note: Output is float32 probability; kept in float only at the loss boundary
Conv1d / Conv1dTransposed
src/layer/Conv1d.c
Fwd: 1-D convolution over temporal MFCC features
Bwd: Gradient w.r.t. input and kernel computed via correlation
Note: Transposed variant for potential encoder-decoder future work
SGD Optimizer (src/optimizer/Sgd.c) — w ← w − lr·∂L/∂w + momentum + weight decay. State: velocity buffer per parameter. Configurable for FLOAT32 or INT8 mode.

## Slide 15
Implementation — Training Loop & Data Loading
TrainingLoopApi
trainingRun()
Top-level entry point. Accepts model[], loss fn, train/eval dataloaders, optimizer, and epoch callback.
TrainingEpochDefault
Iterates over all batches in an epoch. Calls training batch, accumulates loss, triggers eval.
TrainingBatchDefault
Processes a single mini-batch. Calls forward → loss → backward → optimizer step.
CalculateGradsSequential
Sequential backpropagation. Walks the layer array in reverse, accumulates gradient tensors.
inferenceWithLoss()
Eval pass: forward only, computes loss + accuracy + precision + recall + F1 per epoch.
epochCallback()
User-supplied hook called after each epoch. In MNIST experiment: writes row to CSV log.
Data Loading
DataLoaderApi
Generic loader with configurable batch size, shuffle, and sample callback.
NPYLoader
Parses NumPy .npy binary format to load pre-computed features or datasets.
CSVHelper
Writes training logs (epoch, loss, acc, P/R/F1) for post-hoc analysis.
Model Serialization
Serialize.c / Deserialize.c enable saving and loading model weights to binary buffers — essential for resuming training on-device or transferring weights via UART.

## Slide 16
Validation Experiment — MNIST on Host PC
Purpose: Validate the full training pipeline (forward, backward, SGD, loss, dataloader, CSV logging) end-to-end on a known benchmark before deploying to MCU. MNIST is the canonical first test: simple, well-understood, and fast to converge.
Model
Input: 28×28 → flatten → 784
Linear 784 → 20
ReLU
Linear 20 → 10
Softmax
Optimizer: SGD lr=0.001
Batch size: 32 | Epochs: 10
Loss: Cross-Entropy
MnistExperiment.c — Training Entry Point
trainingRun(
model, MODEL_SIZE, CROSS_ENTROPY,
trainDataloader, testDataloader,
sgd, // lr=0.001, no momentum
10, // epochs
calculateGradsSequential,
inferenceWithLoss,
epochCallback // → CSV log
);
// Logs: epoch, train_loss, eval_loss,
// accuracy, precision, recall, f1

## Slide 17
Next: Integrating FQT + RigL — The Core Novelty
This is the thesis contribution. Both FQT (Deutel) and RigL (Evci) exist separately — combining them under MCU constraints is novel. The main integration challenges are listed below.
C1
Sparse Mask Representation
RigL requires tracking which weights are active. On MCU, storing a dense bitmask for each layer. For 90% sparsity on a 784×20 layer: only 1568 active weights → 196-byte mask.
C2
int8 Gradient for RigL Grow Step
RigL's grow step requires computing ∂L/∂w for all (including inactive) weights — not just the active ones. This is expensive: need a full dense gradient pass at topology-update steps. FQT must handle this in int8.
C3
Quantization of Sparse Weights
Scale/zero-point must be computed over only the active weights at each step. Inactive weights are zeroed. Re-quantization after topology update must not disturb other active weights' scales.
C4
Memory Budget for Topology Update
During the grow step, a temporary dense gradient buffer is needed. For W=(784×20): 15,680 int32 values = 61 KB. Must fit within 320 KB alongside activations and model buffers.
C5
Topology Update Frequency
RigL updates topology every Δt steps. On MCU, Δt must be tuned: too frequent → extra compute; too rare → poor sparse topology found. Expected range: every 100–500 batch steps.
C6
Backward Pass Through Sparse Linear
In the backward pass, only active connections contribute ∂L/∂W. ∂L/∂x still requires a full (dense) Wᵀδ product for correct gradient propagation. Must implement sparse-weight dense-backward efficiently.

## Slide 18
Revised Milestones — C1 through C11
DONE
C1–C3
Tensor, Arithmetic, Static Allocator
Core data structures, all arithmetic ops, int8/float dtype support, arena allocator
DONE
C4
Layer System (Linear, ReLU, Softmax, Conv1d)
Forward + backward for all basic layers. Parameter management via parameter_t
DONE
C5
SGD Optimizer + Training Loop
Full training loop with batch/epoch management, loss, eval metrics, CSV logging
DONE
C6
Data Loading: NPY + DataLoader API
Load .npy datasets, generic dataloader with batching and shuffle support
DONE
C7
MNIST Validation Experiment
End-to-end dense float32 training on MNIST. Baseline confirmed working.
NEXT
C8
Quantization Layer + FQT Backward
QuantizationLayer.c exists. Next: wire int8 backward pass with proper rounding
TODO
C9
Sparse Mask + RigL Prune/Grow Step
Bitmask-based sparse representation, magnitude prune, gradient-grow topology update
TODO
C10
FQT + RigL Combined Training on Host
Run sparse int8 training on PC host, validate accuracy vs dense float32 baseline
TODO
C11
Port & Profile on STM32 Nucleo-F746ZG
Flash to board, measure latency, peak RAM, energy per epoch. Final thesis results.

## Slide 19
Expected Results & Evaluation Metrics
Classification Accuracy
Target: ≥ 75% on dev-clean
Closed-set ID on 40 speakers. Baseline dense float32 will set the upper bound; FQT+RigL should stay within 5–8 pp.
Peak SRAM Usage
Target: < 256 KB training
320 KB total; leave headroom for stack and HAL. Sparsity at 80% should cut activation + gradient buffer proportionally.
Training Latency per Epoch
Target: < 30 seconds / epoch
Estimate based on Deutel et al. int8 speedups. Sparse matmul further reduces MACs per step.
Energy per Epoch
Target: Measured via INA219
Target hardware will be instrumented. Lower energy demonstrates viability for battery-powered edge devices.
Topology Convergence
Target: Stable after ≤ 50 updates
RigL masks should stabilize; measure Jaccard similarity of mask across consecutive update steps.
Model Size
Target: < 64 KB weights
At 90% sparsity + int8, a 784×20×10 model stores only ~1.6 KB of active weights — well within Flash budget.

## Slide 20
Research Contributions
01
First combined FQT + RigL implementation on MCU
No prior work demonstrates dynamic sparse training under fully quantized int8 arithmetic on a Cortex-M microcontroller. This is the primary novel contribution.
02
Pure-C, zero-dependency on-device training stack
The OnDeviceTraining framework (tensor engine, layers, optimizer, data loader) is written entirely in C with no Python, no PyTorch, no OS — portable to any embedded target.
03
Memory analysis of FQT + RigL under MCU constraints
Characterizes how peak SRAM usage scales with sparsity level, layer sizes, and topology update frequency. Practical design rules for future MCU training work.
04
End-to-end audio → speaker ID training on hardware
MFCC extraction, network training, and inference all running on the F746ZG without host assistance. Demonstrates the feasibility of biometric personalization on resource-constrained devices.

## Slide 21
Thank You
Questions & Discussion
FQT: Deutel et al., 2024 — On-Device Training of Fully Quantized DNNs on Cortex-M RigL: Evci et al., NeurIPS 2020 — Rigging the Lottery Survey: Hoefler et al., JMLR 2021 — Sparsity in Deep Learning