## Slide 1
MASTER'S THESIS PRESENTATION
On-Device Training for
Activity Recognition
Adding RigL Sparse Training to an FQT C Framework | Human Activity Recognition
Mohamed | Based on: Deutel et al. (2024) & Evci et al. (2020) | STM32 Nucleo-F746ZG | UCI HAR Dataset
Cortex-M7 @ 216 MHz | 320 KB RAM | 1 MB Flash | 6-Class Activity Recognition

## Slide 2
What This Thesis Is About
TARGET GOAL
Classify human activities (walking, sitting, standing...) from wrist/waist sensor data — train ON the MCU to adapt to a new user without any server
METHOD
FQT: 8-bit quantized training to save RAM
RigL: Sparse network training to reduce model size — both fit in 320 KB!
HARDWARE
STM32 Nucleo-F746ZG
Cortex-M7 @ 216 MHz
320 KB RAM, 1 MB Flash
Dataset: UCI HAR
Two Foundation Papers:
Paper 1: Deutel et al. (2024)
On-Device Training of Fully Quantized DNNs on Cortex-M MCUs
Paper 2: Evci et al. (2020)
RigL: Rigging the Lottery — Making All Tickets Winners

## Slide 3
PART 1 OF 2
On-Device Training with
Fully Quantized Training (FQT)
Deutel, Hannig, Mutschler & Teich — arXiv:2407.10734 — August 2024
Problem: DNNs deployed on MCUs use quantized 8-bit weights for inference — but training is always done in float32 on GPU servers. Can we train IN PLACE on the MCU without any conversion?

## Slide 4
Why Train ON the Device?
The model must adapt to a new user's movement patterns AFTER deployment — without sending sensor data to a server
Sensor Privacy
Body movement data reveals biometric identity. On-device training means raw sensor data never leaves the wearable — no server ever receives your motion patterns.
Works Offline
Wearables are often used in areas with no connectivity. On-device adaptation works completely offline — essential for field-deployed health or industrial sensors.
Massive Energy Savings
MCUs consume 0.01–0.15 W. GPU training: 300 W. On-device training is orders of magnitude more efficient — enabling battery-powered operation.
Personalization On-Device
The model adapts to a specific user's gait and movement style on the fly — personalization without reprogramming or sending data to a cloud server.

## Slide 5
Neural Network Core Equations
Every neural network layer has three equations — two for learning, one for inference
→
FORWARD PASS (Inference — same during training)
Yₙ = Wₙ · Xₙ
Compute the output of layer n. Wₙ = weight matrix, Xₙ = input tensor, Yₙ = output. Runs identically during inference AND training — but Xₙ must be STORED during training for Eq. 2.
Eq.1
ERROR PROPAGATION (Backward pass)
Eₙ₋₁ = WₙᵀEₙ
Propagate the error signal backward through the network. Eₙ = error at layer n, Wₙᵀ = transposed weights.
Eq.2
WEIGHT GRADIENT [Eq. 2]
∇Wₙ = Eₙ · Xₙᵀ
Compute the gradient for each weight. Eₙ = error signal, Xₙᵀ = transposed input stored during forward pass. This is why activations cannot be discarded during the forward pass!

## Slide 6
The Core Challenge: Memory
Training requires 4–10× more RAM than inference — the MCU simply doesn't have that much
1
Intermediate Tensors Can't Be Discarded
During inference: each layer output is used immediately then thrown away to free RAM. During training: every layer output must be KEPT in memory until the backward pass needs it.
2
Minibatches Add a Batch Dimension
SGD processes B samples at once. This adds a new dimension to all tensors: e.g., [1×28×28] becomes [48×28×28] for batch size 48, multiplying RAM use 48×.
3
Weights Must Be in RAM, Not Flash
Flash memory is read-only. Trainable weights that get dynamically updated at runtime must be in RAM.
4
Backward Pass ≈ 2× Forward Pass Cost
For each trainable layer, backpropagation must compute two additional matrix multiplications: one for the error signal, one for the weight gradient.
Solution: Use 8-bit quantization throughout (FQT) to cut all tensor sizes by 4× + skip low-importance gradients

## Slide 7
Key Concept 1: Quantization
Reducing numerical precision to save memory and accelerate computation on integer hardware
Analogy
float32: weight = 0.38247631 (4 bytes)
uint8: weight = 97 (1 byte)
You lose some decimal precision, but save 75% memory. MCUs execute integer operations 4x faster than float!
The Quantization Formula
vq =( vf / s ) + z
vf = original float value
s = scale: stretch factor from the tensor min/max range
z = zero point: integer offset so zero maps to zero
Memory Impact at Scale:
float32 (32 bits)
500K params = 2.0 MB
int16 (16 bits)
500K params = 1.0 MB
uint8 (8 bits)
500K params = 0.5 MB <- FQT

## Slide 8
FQT: Fully Quantized Error Propagation
Eq. 4 — Quantized version of Eq. 1. to make all values are integers with scale and zero-point adjustments.
Eq. 1 (Standard float32):
E_(n-1) = WₙT · Eₙ
↓ Fully Quantized Version ↓
Eq. 4
e(n-1) = [(sW_n · se_n / sen-1)
× (W_n − zW_n) · (en − ze_n)] + ze_(n-1)
s^W = weight scale | s^E = error scale | z = zero-point offset | W^q, E^q = quantized integer matrices
Eq. 3 — Gradient: No Requantization
The quantized version of Eq. 2 (∇W = E·Xᵀ) looks identical to Eq. 2. The paper OMITS requantization — gradient passes directly to SGD (Eq. 5) as-is, without being re-encoded as uint8.

## Slide 9
FQT: Quantized SGD Weight Update
Three equations that update quantized weights after each minibatch — adapted from standard SGD. Only one mini_batch need to be stored in RAM
Step 1 — Basic Quantized Weight Update [Eq. 5]
w_(i+1) = (1/sw_(i+1)) * [ (w_i - zw_i)*sw_i - l * grad_w_i ] + zw_(i+1)
l = learning rate | s = scale | z = zero point | grad_w = gradient | subscript i = current step
Step 2 — Dynamic Scale & Zero-Point [Eq. 6, 7]
s_(i+1) = (f_max - f_min) / 255
z_(i+1) = floor( -f_min / s_(i+1) )
Adjusts the quantization range dynamically as weights shift.
Step 3 — Standardized Gradient Update [Eq. 8]
Normalizes gradient with running mean(0) & std dev(1): mu, sigma. Prevents 8-bit overflow. Critical for stable quantized training!
Intuition: Like a teacher normalizing exam scores before deciding grade adjustments — prevents different scales from causing wildly different update magnitudes. This keeps all 8-bit weights updating consistently across all channels.

## Slide 10
PART 2 OF 2
Sparse Dynamic Training
with RigL
Evci, Gale, Menick, Castro & Elsen — ICML 2020 | github.com/google-research/rigl
Problem: Most methods that yield sparse networks require training a full dense model first. Can we train sparse from scratch and STILL beat dense-to-sparse results?

## Slide 11
Why Sparse Neural Networks?
Most weights in a trained neural network can safely be set to zero
Smaller Model Size
A 90% sparse model stores only 10% of the original weights -> 10x smaller. A model that doesn't fit on an STM32 might fit after sparsification.
Faster Inference
Multiplying by zero can be skipped entirely. Sparse formats enable real speedups on hardware with sparse acceleration.
Enables Larger Models
Train a sparse model 10x larger than the largest trainable dense model on your hardware — without needing a dense version first.

## Slide 12
From Lottery Tickets to RigL
The theoretical motivation and why existing approaches fall short
The Lottery Ticket Hypothesis (2019)
Inside every large dense network there exists a tiny 'winning ticket' subnetwork — a sparse network with the right initial weights — that could have been trained to the same accuracy from scratch.
Problem: You only find the ticket AFTER training the dense network!
Dense-to-Sparse Pruning (Classic Approach)
1. Train full dense model (300-400 GPU-hours for ResNet)
2. Prune weights below a threshold
3. Fine-tune the pruned network
Limitations:
- Wasteful — computes zero-valued weights for 90% of training
- Max sparse model = max dense model you can train
RigL's Breakthrough
Start with a SPARSE network (e.g., 90% zeros) -> Train with fixed parameter count -> Every T steps: DROP small weights + GROW high-gradient zeros
No dense model ever needed. Memory and FLOPs are proportional to SPARSITY throughout. Achieves higher accuracy than pruning at the same compute budget!

## Slide 13
RigL Algorithm: The 5 Key Steps
Full pseudocode walkthrough — from initialization to convergence
Init
Randomly sparsify the network
Start from a dense network. Randomly zero out weights until target sparsity S (e.g., 90%). Gives a sparse but untrained starting point.
Train
Normal training steps (repeat T times)
Run standard minibatch SGD on the sparse network. Only non-zero weights receive updates. Most computation skipped for zero weights.
Drop
Remove weak connections (every T steps)
Find the k active connections with SMALLEST absolute weight value: I_drop = ArgTopK(-|theta_l|, k). Set them to zero.
Grow
Activate new connections
Compute gradients for ALL zero weights. Find the k zeros with LARGEST gradient magnitude: I_grow = ArgTopK(|grad L|, k). Initialize new to ZERO.
End
Stop mask updates at iteration T_end
After T_end iterations, freeze the sparse mask. Final training refines weight values only. Slight delay improves accuracy.

## Slide 14
Sparsity Distribution: Erdős-Rényi-Kernel (ERK)
Best method for CNNs — allocates higher sparsity to large layers, lower sparsity to small ones
ERK Sparsity Formula:
sˡ ∝ (nˡ⁻¹ + nˡ + wˡ + hˡ) / (nˡ⁻¹ × nˡ × wˡ × hˡ)
nˡ⁻¹
Input channels
Conv1: 9 (raw sensor channels)
nˡ
Output channels
Conv1: 16
wˡ
Kernel width
Conv1: 7 (filter size)
hˡ
Kernel height
Conv1: 1 (1D conv → height = 1)
nˡ⁻¹×nˡ×wˡ×hˡ
Total possible weights (denominator)
Conv1: 9×16×7×1 = 1,008 — grows fast
nˡ⁻¹+nˡ+wˡ+hˡ
Sum of dimensions (numerator)
Conv1: 9+16+7+1 = 33 — grows slowly

## Slide 15
RigL Update Schedule
Four parameters control when to update, how often, how aggressively, and how that aggression decays over time
T
Update Interval
Number of normal SGD steps between each DROP+GROW topology update.
T_end
Stop Updating At
Training iteration at which topology updates permanently stop. After T_end the sparse mask is frozen — only weight values continue to update.
α
Initial Fraction
Starting fraction of active connections to replace at each update. k = α × (1−sˡ) × Nˡ connections dropped and grown. e.g. α=0.3 → replace 30% of active connections.
f_decay
Decay Function
Called every T steps. Returns the current fraction αₜ. Decays α from its initial value down to zero by T_end. RigL uses cosine annealing.
f_decay
(cosine)
αₜ = α/2 × (1 + cos(π × t / T_end))
t=0 → αₜ=α (maximum) t=T_end/2 → αₜ=α/2 t=T_end → αₜ=0 (mask freezes)

## Slide 16
RigL: DROP — Removing Weak Connections
Every T steps — remove the k connections with smallest absolute weight value
I_drop = ArgTopK( −|θˡ| , k )
where k = ( αₜ × (1−sˡ) × Nˡ )
I_drop
The set of connection INDICES to remove — mask set from 1→0 at these positions
ArgTopK(v, k)
Returns the k positions in vector v with the LARGEST values — indices, not values themselves
θˡ
Vector of all currently ACTIVE (non-zero) weight values in layer l
|θˡ|
Absolute values of weights — removes the sign, keeping only how large each weight is
−|θˡ|
NEGATED magnitudes — trick to make smallest magnitudes become the largest values, so ArgTopK finds the WEAKEST connections
k
Number of connections to drop = (αₜ × active_count). Equal to the number that will be grown — keeps total fixed
Why weight magnitude? |w| ≈ importance.
A weight near zero (0.001) multiplied by any input produces a near-zero output — functionally invisible to the network. Removing it causes almost no loss increase. Large weights (0.85) strongly affect output — never drop those. Magnitude requires no extra forward/backward pass.

## Slide 17
RigL: GROW — Activating Promising Connections
The novelty of RigL — grow connections guided by gradient magnitude, not randomly
I_grow = ArgTopK( |∇_Θˡ Lₜ| , k )
search is over zero-weight positions only (Θˡ \ I_drop)
I_grow
The set of connection INDICES to activate — mask set from 0→1 at these positions
|∇_Θˡ Lₜ|
Absolute gradient magnitude at each position in layer l at iteration t — including ZERO-WEIGHT positions
Θˡ \ I_drop
Search space: all zero-weight positions EXCEPT those just dropped (don't immediately re-add what you just removed)
k
Exactly equal to the number just dropped — parameter count stays perfectly fixed after both steps
Why gradient of ZERO weights?
A zero weight contributes nothing to the output — but its gradient tells you: 'if this connection existed, how much would the loss decrease?' Large |∇| at a zero = this connection is urgently needed right now.
New connections initialized to ZERO
weight=0 means output unchanged at the moment of activation. No sudden loss spike. The new connection immediately starts receiving SGD gradient updates from the very next training step.
vs SET (random growth): RigL's only difference from SET is this GROW step. Random activation = blind guessing. Gradient-guided = using the loss landscape to pick exactly the connections the network currently needs most. This single change accounts for most of RigL's accuracy gain.

## Slide 18
Combining FQT + RigL for HAR on STM32
How the two methods complement each other — your thesis adds RigL to the existing FQT C framework
FQT (Deutel et al.)
8-bit integer weights & activations
Seamless inference & training
Dynamic quantization parameters
Standardized gradient SGD
-> Solves the MEMORY problem
+
RigL (Evci et al.)
Sparse topology from the start
Gradient-guided connection growth
ERK sparsity distribution
No dense model ever needed
Fixed parameter count throughout
-> Solves the MODEL SIZE problem

## Slide 19
Implementation Sequence: Step-by-Step Technical Guide
1
Architecture
Define Model Architecture
1D CNN from C code: 3× Conv1d blocks + Linear head. ~10,214 params. Target: >90% HAR accuracy before adding sparsity. Verify architecture matches existing C framework.
2
Data
UCI HAR Sensor Data Pipeline
Load .npy files (train_x: [N,9,128], train_y: [N]). Normalize per-channel to [-1,1]. Build DataLoader with batch=64. Verify: 6 classes balanced across 10,299 total samples.
3
Baseline
Train Dense Float32 Baseline
Train for 30-50 epochs, Adam optimizer, LR=1e-3, batch=64. Target: >85% accuracy on dev set. This is your ceiling for all future experiments.
4
RigL
Apply RigL Sparse Training
Wrap SGD with RigL: every T=100 steps, drop k bottom-magnitude, grow k top-gradient zeros. Use ERK distribution at 80% target sparsity. Validate: >83% accuracy.
5
FQT
Post-Training Quantize + FQT Backward Pass
Calibrate scale/zero-point per tensor. Convert to uint8. Implement Eq.1-8 (quantized backprop + standardized SGD). Test FQT accuracy on desktop simulation.
6
STM32
Port to rp20350a with CMSIS-NN
Convert tensors to C arrays (xxd -i model.bin). Use arm_convolve_HWC_q7() for conv, arm_fully_connected_q7() for FC. Use DWT cycle counter to profile latency.
7
Training
On-Device Transfer Learning Experiments
Reset last 2 layers to random. On-device training: 10-20 epochs, 48 samples/batch (sequential). Measure per-sample latency (ms), RAM peak (KB), accuracy after each epoch.
8
Eval
Benchmarking & Analysis
Compare: float32 vs FQT vs FQT+RigL. Plot accuracy vs RAM vs latency. Check convergence curves. Ablation: how much does each component contribute independently?