## Slide 1
MASTER'S THESIS PRESENTATION
On-Device Training for
Activity Recognition
Adding RigL Sparse Training to an FQT C Framework | Human Activity Recognition
Mohamed | Based on: Deutel et al. (2024) & Evci et al. (2020) | STM32 Nucleo-F746ZG | UCI HAR Dataset
Cortex-M7 @ 216 MHz | 320 KB RAM | 1 MB Flash | 6-Class Activity Recognition

## Slide 2
What This Thesis Is About
TARGET GOAL
Classify human activities (walking, sitting, standing...) from wrist/waist sensor data — train ON the MCU to adapt to a new user without any server
METHOD
FQT: 8-bit quantized training to save RAM
RigL: Sparse network training to reduce model size — both fit in 320 KB!
HARDWARE
STM32 Nucleo-F746ZG
Cortex-M7 @ 216 MHz
320 KB RAM, 1 MB Flash
Dataset: UCI HAR
Two Foundation Papers:
Paper 1: Deutel et al. (2024)
On-Device Training of Fully Quantized DNNs on Cortex-M MCUs
Paper 2: Evci et al. (2020)
RigL: Rigging the Lottery — Making All Tickets Winners

## Slide 3
PART 1 OF 2
On-Device Training with
Fully Quantized Training (FQT)
Deutel, Hannig, Mutschler & Teich — arXiv:2407.10734 — August 2024
Problem: DNNs deployed on MCUs use quantized 8-bit weights for inference — but training is always done in float32 on GPU servers. Can we train IN PLACE on the MCU without any conversion?

## Slide 4
What is a Microcontroller (MCU)?
Think of it as a tiny, very cheap computer built into everyday devices (watches, thermostats, medical sensors)
Component | GPU Server (Training) | Smartphone | MCU — Our Target ✓
CPU | 3–4 GHz, 32+ cores | 3 GHz, 8 cores | 64–600 MHz, 1 core
RAM | 80–400 GB | 8–16 GB | 256 KB – 2 MB (!)
Storage | Terabytes | 128–512 GB | 1–16 MB Flash
Power Draw | 300–400 Watts | 3–5 Watts | 0.01–0.15 Watts
Cost | $5,000+ | $200+ | $2–$25
Our Board | — | — | STM32 Nucleo-F746ZG
Key Insight: MCUs consume 1000x less power than GPU servers. Training locally = privacy + energy savings + no connectivity required.

## Slide 5
Why Train ON the Device?
The model must adapt to a new user's movement patterns AFTER deployment — without sending sensor data to a server
Sensor Privacy
Body movement data reveals biometric identity. On-device training means raw sensor data never leaves the wearable — no server ever receives your motion patterns.
Works Offline
Wearables are often used in areas with no connectivity. On-device adaptation works completely offline — essential for field-deployed health or industrial sensors.
Massive Energy Savings
MCUs consume 0.01–0.15 W. GPU training: 300 W. On-device training is orders of magnitude more efficient — enabling battery-powered operation.
Personalization On-Device
The model adapts to a specific user's gait and movement style on the fly — personalization without reprogramming or sending data to a cloud server.

## Slide 6
The Core Challenge: Memory
Training requires 4–10× more RAM than inference — the MCU simply doesn't have that much
1
Intermediate Activations Can't Be Discarded
During inference: each layer output is used immediately then thrown away to free RAM. During training: every layer output must be KEPT in memory until the backward pass needs it.
2
Minibatches Add a Batch Dimension
SGD processes B samples at once. This adds a new dimension to all tensors: e.g., [1×28×28] becomes [48×28×28] for batch size 48, multiplying RAM use 48×.
3
Weights Must Be in RAM, Not Flash
Flash memory (where code lives) is read-only. Trainable weights that get updated at runtime must be in RAM — the most precious and scarce resource on the MCU.
4
Backward Pass ≈ 2× Forward Pass Cost
For each trainable layer, backpropagation must compute two additional matrix multiplications: one for the error signal, one for the weight gradient.
Solution: Use 8-bit quantization throughout (FQT) to cut all tensor sizes by 4× + skip low-importance gradients

## Slide 7
Key Concept 1: Quantization
Reducing numerical precision to save memory and accelerate computation on integer hardware
Analogy
float32: weight = 0.38247631 (4 bytes)
uint8: weight = 97 (1 byte)
You lose some decimal precision, but save 75% memory. MCUs execute integer operations 4x faster than float!
The Quantization Formula
vq = floor( vf / s ) + z
vf = original float value
s = scale: stretch factor from the tensor min/max range
z = zero point: integer offset so zero maps to zero
Memory Impact at Scale:
float32 (32 bits)
500K params = 2.0 MB
int16 (16 bits)
500K params = 1.0 MB
uint8 (8 bits)
500K params = 0.5 MB <- FQT
STM32 Nucleo-F746ZG has only 320 KB RAM. uint8 is the only format that lets a useful model + training overhead fit!

## Slide 8
Key Concept 2: QAT vs FQT
Two approaches to training quantized networks — only one works on a tiny MCU
Quantization-Aware Training (QAT)
Trains in FLOAT32 throughout
Quantization is only SIMULATED
Fake quantization nodes inserted
Must convert model before/after
RAM savings: ZERO during training
Requires costly conversion step
Cannot be used for in-place on-device training — model must be float32 in memory!
Fully Quantized Training (FQT) <- This paper
Trains with REAL uint8 integers
Forward AND backward: both quantized
Same model format for inference AND training
No conversion ever needed
4x less memory for all tensors
Integer ops faster on Cortex-M MCUs
Model lives in memory exactly the same way during inference and training. Zero overhead for switching modes!

## Slide 9
Key Concept 3: Backpropagation (Backprop)
The algorithm that allows neural networks to learn — computing how each weight should change
Analogy: Imagine adjusting guitar strings. You pluck, hear the wrong note (loss), then slightly tighten/loosen each string (weights) based on how much each one contributed to being off-key. Repeat thousands of times until in tune.
The 3 Core Equations:
Forward Pass [Eq. 3]
Yn = Wn * Xn
Compute layer output. Wn=weights, Xn=input, Yn=output. In FQT: all are uint8, result is int32.
Error Propagation [Eq. 1]
En-1 = WnT * En
Propagate the error backward. En=error at layer n, WnT=transposed weights. Same math as forward, just transposed!
Weight Gradient [Eq. 2]
Grad_Wn = En * XnT
Compute how much each weight contributed to the error. Used by SGD to update the weights.
Key Insight: Eq.1 and Eq.2 are both transposed versions of Eq.3 — the SAME quantization kernel used for inference works for training too!

## Slide 10
FQT: Quantized SGD Weight Update
Three equations that update quantized weights after each minibatch — adapted from standard SGD
Step 1 — Basic Quantized Weight Update [Eq. 5]
w_(i+1) = (1/s_(i+1)) * [ (w_i - z_i)*s_i - l * grad_w_i ] + z_(i+1)
l = learning rate | s = scale | z = zero point | grad_w = gradient | subscript i = current step
Step 2 — Dynamic Scale & Zero-Point [Eq. 6, 7]
s_(i+1) = (f_max - f_min) / 255
z_(i+1) = floor( -f_min / s_(i+1) )
Adjusts the quantization range dynamically as weights shift — like QAT but done at runtime!
Step 3 — Standardized Gradient Update [Eq. 8]
Normalizes gradient with running mean & std dev: mu, sigma. Prevents 8-bit overflow. Critical for stable quantized training!
Intuition: Like a teacher normalizing exam scores before deciding grade adjustments — prevents different scales from causing wildly different update magnitudes. This keeps all 8-bit weights updating consistently across all channels.

## Slide 11
Dynamic Sparse Gradient Updates
Skip computing gradients for layers where they won't matter much — up to 8.7x speedup!
3 Observations Behind This Idea:
a
Gradients shrink through the backward pass
Earlier layers receive very small error signals — updating their weights rarely leads to meaningful improvement.
b
Sparse activation patterns dominate
For any given input sample, only a few neurons activate strongly. Most gradient values for that sample are near zero.
c
As training succeeds, fewer gradients matter
A well-trained model uses smaller, tighter neuron clusters per class. Fewer updates needed as the loss converges.
The Dynamic Update Rate [Eq. 9]:
k = floor( min{ l_min + |e|(l_max - l_min), 1 } * N )
k = # gradients to compute. l_min/l_max control how aggressively to skip. |e| = normalized loss (0=converged). As loss -> 0, k -> l_min*N — fewer updates computed over time!

## Slide 12
FQT Paper: Results
Evaluated on 11 datasets across Cortex-M0+, M4, and M7 microcontrollers
34.8%
Less RAM
vs MCUNet
49.0%
Lower latency
per sample
8.7x
Speedup with
dynamic gradients
~86%
Accuracy on
CIFAR-10 (FQT)
Transfer Learning Accuracy — Test Accuracy After 20 Epochs On-Device
Chart: 
| CWRU | Daliac | CIFAR-10 | Animals | Speech | CIFAR-100
FQT (uint8) | 99.5 | 97.1 | 85.8 | 84.2 | 81.4 | 40.4
Float32 | 99.8 | 96.5 | 85.6 | 89.2 | 84.3 | 54.5
GPU Baseline | 99.8 | 96.5 | 86.5 | 86.4 | 90.1 | 59.8

## Slide 13
PART 2 OF 2
Sparse Dynamic Training
with RigL
Evci, Gale, Menick, Castro & Elsen — ICML 2020 | github.com/google-research/rigl
Problem: Most methods that yield sparse networks require training a full dense model first. Can we train sparse from scratch and STILL beat dense-to-sparse results?

## Slide 14
Why Sparse Neural Networks?
Most weights in a trained neural network are redundant and can safely be set to zero
Analogy: Your brain has ~86 billion neurons but uses only a tiny fraction for any single task. When you read, vision and language neurons activate — not the ones for riding a bike. Neural networks work the same way: most weights contribute almost nothing to any given prediction.
Smaller Model Size
A 90% sparse model stores only 10% of the original weights -> 10x smaller. A model that doesn't fit on an STM32 might fit after sparsification.
Faster Inference
Multiplying by zero can be skipped entirely. Sparse formats enable real speedups on hardware with sparse acceleration.
Better Generalization
Sparsity acts as implicit regularization — some 50% sparse models actually outperform their dense counterparts on test accuracy.
Enables Larger Models
Train a sparse model 10x larger than the largest trainable dense model on your hardware — without needing a dense version first.

## Slide 15
From Lottery Tickets to RigL
The theoretical motivation and why existing approaches fall short
The Lottery Ticket Hypothesis (2019)
Inside every large dense network there exists a tiny 'winning ticket' subnetwork — a sparse network with the right initial weights — that could have been trained to the same accuracy from scratch.
Problem: You only find the ticket AFTER training the dense network!
Dense-to-Sparse Pruning (Classic Approach)
1. Train full dense model (300-400 GPU-hours for ResNet)
2. Prune weights below a threshold
3. Fine-tune the pruned network
Limitations:
- Wasteful — computes zero-valued weights for 90% of training
- Max sparse model = max dense model you can train
RigL's Breakthrough
Start with a SPARSE network (e.g., 90% zeros) -> Train with fixed parameter count -> Every T steps: DROP small weights + GROW high-gradient zeros
No dense model ever needed. Memory and FLOPs are proportional to SPARSITY throughout. Achieves higher accuracy than pruning at the same compute budget!
Key innovation: Instead of random growth (like SET), RigL uses gradient magnitudes to activate the most PROMISING zero connections.

## Slide 16
RigL Algorithm: The 5 Key Steps
Full pseudocode walkthrough — from initialization to convergence
Init
Randomly sparsify the network
Start from a dense network. Randomly zero out weights until target sparsity S (e.g., 90%). Gives a sparse but untrained starting point.
Train
Normal training steps (repeat T times)
Run standard minibatch SGD on the sparse network. Only non-zero weights receive updates. Most computation skipped for zero weights.
Drop
Remove weak connections (every T steps)
Find the k active connections with SMALLEST absolute weight value: I_drop = ArgTopK(-|theta_l|, k). Set them to zero.
Grow
Activate promising connections
Compute gradients for ALL zero weights. Find the k zeros with LARGEST gradient magnitude: I_grow = ArgTopK(|grad L|, k). Initialize new to ZERO.
End
Stop mask updates at iteration T_end
After T_end iterations (~3/4 of training), freeze the sparse mask. Final training refines weight values only. Slight delay improves accuracy.

## Slide 17
RigL: DROP and GROW in Detail
The topology update is what makes RigL special — gradient-guided growth vs random growth
DROP — Remove Weak Connections
Criterion: Smallest absolute weight value:
I_drop = ArgTopK( -|theta_l| , k )
theta_l = weights in layer l, k = connections to drop
Rationale: Small absolute weights barely affect output. Removing them causes almost no loss increase. Pruning dry branches that contribute nothing to the tree.
Fraction k decreases over time via cosine annealing:
k_t = alpha/2 * (1 + cos(pi*t/T_end))
Starts aggressive, becomes conservative.
After drop: positions become zero — sparse mask is updated
GROW — Activate Promising Connections
Criterion: Largest gradient magnitude on zero weights:
I_grow = ArgTopK( |grad_L| , k )
grad_L = loss gradient including zero weights
k = same number just dropped
Key innovation: A zero weight with large gradient magnitude would reduce the loss fastest if activated. This is what beats random growth (SET).
Critical: New connections initialized to ZERO.
Network output doesn't change on connection add — no sudden loss spikes. Weight immediately starts getting gradient updates.
Dense gradients can be discarded after grow — no permanent storage needed

## Slide 18
Sparsity Distributions: How to Allocate Zeros Across Layers
Not all layers should have the same sparsity — small layers need more capacity
1. Uniform
s_l = S (same for every layer)
Every layer has the same sparsity S. Simple but sub-optimal — small final layers lose too much capacity at high sparsity.
+ Simple, predictable FLOP count
- Hurts accuracy at high sparsity; small layers starved
2. Erdos-Renyi
s_l proportional to 1 - (n_(l-1)+n_l)/(n_(l-1)*n_l)
Inspired by random graph theory. Layers with MORE parameters get HIGHER sparsity; smaller layers stay denser to preserve capacity.
+ Better accuracy for fully-connected layers
- Not designed for convolutional kernels
3. Erdos-Renyi-Kernel (ERK) <- Best for CNNs!
s_l proportional to 1 - (n_(l-1)+n_l+w_l+h_l)/(n_(l-1)*n_l*w_l*h_l)
Extends ER to include kernel width (w_l) and height (h_l). Early conv layers (large spatial dims) get lower sparsity — exactly where you need capacity.
+ State-of-the-art accuracy; used in all best RigL results
- ~2x more FLOPs than uniform for same parameter count

## Slide 19
RigL Results: State-of-the-Art Sparse Training
ResNet-50 on ImageNet-2012 — all methods at 80% sparsity unless noted
Chart: 
| Dense (ref) | Static Sparse | SNIP | SET | SNFS | RigL | RigL 5x | RigL 5x ERK
Top-1 Accuracy (%) | 76.8 | 70.6 | 72 | 72.9 | 74.2 | 74.6 | 76.6 | 77.1
77.1%
RigL 5x ERK
(vs 76.8% dense!)
0.23x
Training FLOPs
vs dense baseline
+3.2%
Over best pruning
at 90% sparsity
Remarkable: RigL (80% sparse, 5x training) equals the DENSE model accuracy while using only 23% of training FLOPs!

## Slide 20
Combining FQT + RigL for HAR on STM32
How the two methods complement each other — your thesis adds RigL to the existing FQT C framework
FQT (Deutel et al.)
8-bit integer weights & activations
Seamless inference & training
Dynamic quantization parameters
Standardized gradient SGD
Dynamic sparse gradient updates
-> Solves the MEMORY problem
+
RigL (Evci et al.)
Sparse topology from the start
Gradient-guided connection growth
ERK sparsity distribution
No dense model ever needed
Fixed parameter count throughout
-> Solves the MODEL SIZE problem
= Sparse + Quantized + On-Device Activity Recognition
FQT framework exists in C -> Add RigL mask update -> 1D CNN with ~10K params, 80% sparse, fits easily in 320 KB RAM!

## Slide 21
HAR Model Architecture — 1D CNN (from C Implementation)
3 × (Conv1d + ReLU + Pool) + Flatten + Linear + Softmax = 12 layers in C
Input Sensor Data
[9 channels × 128 steps]
Block 1
Conv1d (9→16, K=7)
ReLU
MaxPool(2,2)
Block 2
Conv1d (16→32, K=5)
ReLU
MaxPool(2,2)
Block 3
Conv1d (32→64, K=3)
ReLU
AvgPool(32,32)
[16 × 64]
[32 × 32]
[64 × 1]
Flatten [64]
Linear(64 → 6)
Softmax [6 classes]
Predicted Activity
Parameter Count & Memory Footprint:
Layer | Params | float32 | uint8 (FQT) | uint8 + 80% sparse
Conv1 (9→16, K=7) | 1,024 | 4.0 KB | 1.0 KB | ~0.2 KB
Conv2 (16→32, K=5) | 2,592 | 10.1 KB | 2.5 KB | ~0.5 KB
Conv3 (32→64, K=3) | 6,208 | 24.2 KB | 6.1 KB | ~1.2 KB
Linear (64→6) | 390 | 1.5 KB | 0.4 KB | ~0.1 KB
TOTAL | 10,214 | 39.9 KB | ~10 KB | ~2 KB ✓
6 HAR Classes:
Walking
Upstairs
Downstairs
Sitting
Standing
Laying

## Slide 22
Target Hardware: STM32 Nucleo-F746ZG
The target board for your thesis — same as used in the Deutel FQT paper (IMXRT2062 is close equivalent)
Specification | Value | Relevance for Your Thesis
CPU Core | ARM Cortex-M7 @ 216 MHz | Highest-performance Cortex-M core — FPU + DSP available
RAM (SRAM) | 320 KB total | PRIMARY CONSTRAINT: holds activations + weights + gradients
Flash | 1 MB internal | Stores static weights + code (read-only during training)
FPU | Double-precision FPU | Enables mixed-precision: float32 for some ops, int8 for others
DSP / SIMD | Yes — 4x int8 per cycle | CMSIS-NN exploits this: 4x throughput on quantized layers
Power | ~150 mW active | 1000x less than GPU servers — enables battery-powered use
Price | ~$25 (development board) | Affordable for thesis prototyping
Memory Budget: HAR model is SMALL (~10K params). uint8 weights: ~10 KB. Sparse (80%): ~2 KB! Activations peak at ~50 KB. Total: well under 320 KB. RigL+FQT is MORE than adequate for HAR — validates methodology at low risk.

## Slide 23
Implementation Roadmap: 16 Weeks
A systematic plan: validate each layer before building the next
Phase 1
Wks 1-2
Environment & Tools Setup
Install PyTorch, STM32CubeIDE, CMSIS-NN, cross-compiler (arm-none-eabi-gcc). Verify you can compile + flash a hello-world to the STM32.
Phase 2
Wks 3-4
Data Pipeline & Baseline Model
Download UCI HAR dataset (openml.org or UCI repo). Load .npy sensor files. Train float32 1D CNN baseline on desktop — 3x Conv1d+Pool + Linear, aim for >90% accuracy.
Phase 3
Wks 5-7
RigL Sparse Training
Implement RigL mask update in PyTorch. Test ERK + uniform distributions. Validate that sparse model (80%) retains >83% accuracy. Profile FLOP savings.
Phase 4
Wks 8-10
FQT Quantization & Quantized Training
Post-training quantize the sparse model. Implement quantized backward pass (Eq. 1-8). Test on-device accuracy with FQT. Verify <3% accuracy drop vs float32.
Phase 5
Wks 11-13
STM32 Deployment & On-Device Training
Port model to CMSIS-NN C kernels. Profile RAM, latency/sample, energy per epoch. Run on-device transfer learning (reset final 2 layers, retrain on-device).
Phase 6
Wks 14-16
Evaluation & Thesis Writing
Tabulate: accuracy, RAM usage (KB), latency (ms/sample), energy (mJ/epoch). Compare with float32 baseline and related work. Write thesis chapters.

## Slide 24
Roadmap Detail: Phases 1 & 2
Exact files to create and steps to follow — in order
PHASE 1 — Environment Setup (Weeks 1–2)
First command:
pip install torch numpy scipy scikit-learn matplotlib tqdm
Files to create — in this order:
1
requirements.txt
All packages with pinned versions (torch==2.1.0, numpy, scipy, scikit-learn, matplotlib)
2
config.py
All hyperparameters in ONE file: LR, batch size, IN_CHANNELS=9, LEN_INPUT=128, sparsity=0.8
3
verify_env.py
Import check + torch version + CUDA/MPS check. Run this first every session.
4
CubeIDE: main.c
New STM32 project -> Nucleo-F746ZG -> LED blink loop. Confirms board works.
Success: LED blinks + verify_env.py prints all versions OK
PHASE 2 — Data Pipeline & Baseline (Weeks 3–4)
Download UCI HAR Dataset:
python -c "from sklearn..." # see UCI HAR page
Files to create — in this order:
1
src/dataset.py
HARDataset class: load train_x.npy [N,9,128] + train_y.npy [N] as int labels
2
src/model.py
1D CNN: Conv1d(9->16,K=7)+Pool -> Conv1d(16->32,K=5)+Pool -> Conv1d(32->64,K=3)+AvgPool -> Linear(64,6)
3
src/train_baseline.py
SGD(LR=0.01, momentum=0.9), batch=64, 20 epochs — mirrors the C implementation exactly
4
src/evaluate.py
Load checkpoint, compute top-1 activity accuracy on val split (6 classes)
Success: train_baseline.py reaches >90% accuracy on HAR val set

## Slide 25
Roadmap Detail: Phases 3 & 4
RigL sparse training first — then quantize the sparse 1D CNN model with FQT
PHASE 3 — RigL Sparse Training (Weeks 5–7)
Start by implementing the mask:
mask = torch.ones_like(weight, dtype=torch.bool) # all True
Files — create in this exact order:
1
src/sparse/mask.py
SparseMask class: stores bool tensor per layer, apply() multiplies weights by mask
2
src/sparse/erk.py
ERK sparsity distribution: compute per-layer sparsity using neuron+kernel formula
3
src/sparse/rigl.py
RigLOptimizer: wraps SGD; every T steps runs _drop_and_grow(k) using cosine schedule
4
src/train_rigl.py
Training loop: call rigl.step() instead of optimizer.step(); assert param count constant
Success: 80% sparse model, accuracy drop <3% vs float32 baseline
PHASE 4 — FQT Quantized Training (Weeks 8–10)
Calibration — compute per-layer scale & zero-point:
s=(f_max-f_min)/255 | z=floor(-f_min/s) [Eq. 6, 7]
Files — create in this exact order:
1
src/quantize/calibrate.py
calibrate(model, loader) -> dict of scale & zero_point per layer [Eq.6-7]
2
src/quantize/quant_layers.py
QuantConv2d, QuantLinear: override forward() with uint8 matmul; custom backward() with Eq.1-4
3
src/quantize/fqt_sgd.py
QuantizedSGD: Eq.5 update + Eq.8 standardized gradient (running mean/std per channel)
4
src/train_fqt.py
Replace layers: model = replace_with_quant(model, scales, zp); train with QuantizedSGD
Success: all tensors dtype uint8 at runtime; accuracy within 3% of float32

## Slide 26
Roadmap Detail: Phases 5 & 6
Port to the STM32 board — then measure everything for your thesis
PHASE 5 — STM32 Deployment (Weeks 11–13)
First — export weights as C array:
python export_weights.py -> model_weights.h (auto-generated)
Files — create in this exact order:
1
scripts/export_weights.py
Load .pt checkpoint -> uint8 numpy arrays -> save as .npy per layer
2
scripts/to_c_array.py
Convert .npy to C header: const uint8_t weights_conv1[N] = {0x..., ...};
3
stm32/Src/inference.c
Call arm_convolve_HWC_q7() and arm_fully_connected_q7() in sequence
4
stm32/Src/training.c
On-device backprop: implement Eq.1-9 in C using int8/int32 arithmetic
5
stm32/Src/sensor_window.c
Sliding window buffer for 9-channel IMU data; reads 128-step segments from UART/SPI
Success: inference runs without hard fault; profile RAM with DWT->CYCCNT
PHASE 6 — Evaluation & Thesis (Weeks 14–16)
Experiments to run (in this order):
Dense float32 -> FQT only -> RigL only -> FQT+RigL (your thesis)
Files — create in this order:
1
eval/measure_ram.py
Parse STM32 .map linker file for static RAM; hook _sbrk() for runtime peak
2
eval/benchmark.py
Run all 4 experiments; log accuracy, RAM (KB), latency (ms/sample), energy (mJ)
3
eval/ablation.py
Disable FQT or RigL one at a time; quantify each component's contribution
4
eval/plot_results.py
matplotlib: accuracy curve, RAM bar chart, latency per experiment, convergence
Thesis Table: Accuracy | RAM (KB) | Latency (ms/sample) | Energy (mJ/epoch)

## Slide 27
Implementation Sequence: Step-by-Step Technical Guide
Build each component, validate it, then move on — never skip validation steps
1
Architecture
Define Model Architecture
1D CNN from C code: 3× Conv1d blocks + Linear head. ~10,214 params. Target: >90% HAR accuracy before adding sparsity. Verify architecture matches existing C framework.
2
Data
UCI HAR Sensor Data Pipeline
Load .npy files (train_x: [N,9,128], train_y: [N]). Normalize per-channel to [-1,1]. Build DataLoader with batch=64. Verify: 6 classes balanced across 10,299 total samples.
3
Baseline
Train Dense Float32 Baseline
Train for 30-50 epochs, Adam optimizer, LR=1e-3, batch=64. Target: >85% accuracy on dev set. This is your ceiling for all future experiments.
4
RigL
Apply RigL Sparse Training
Wrap SGD with RigL: every T=100 steps, drop k bottom-magnitude, grow k top-gradient zeros. Use ERK distribution at 80% target sparsity. Validate: >83% accuracy.
5
FQT
Post-Training Quantize + FQT Backward Pass
Calibrate scale/zero-point per tensor. Convert to uint8. Implement Eq.1-8 (quantized backprop + standardized SGD). Test FQT accuracy on desktop simulation.
6
STM32
Port to STM32 with CMSIS-NN
Convert tensors to C arrays (xxd -i model.bin). Use arm_convolve_HWC_q7() for conv, arm_fully_connected_q7() for FC. Use DWT cycle counter to profile latency.
7
Training
On-Device Transfer Learning Experiments
Reset last 2 layers to random. On-device training: 10-20 epochs, 48 samples/batch (sequential). Measure per-sample latency (ms), RAM peak (KB), accuracy after each epoch.
8
Eval
Benchmarking & Analysis
Compare: float32 vs FQT vs FQT+RigL. Plot accuracy vs RAM vs latency. Check convergence curves. Ablation: how much does each component contribute independently?

## Slide 28
Required Textbooks — What to Read & What to Skip
Read these in order — each builds on the last
1
~3 days
Neural Networks and Deep Learning — Michael Nielsen
neuralnetworksanddeeplearning.com (FREE) | WHEN: Week 1 — read BEFORE writing any code
READ: Ch.1: How networks learn (intuition) | Ch.2: Backpropagation in full detail
SKIP: Ch.5-6 (Why deep networks are hard — too theoretical for now)
Why: Best visual explanation of backpropagation that exists. Read Ch.2 twice.
2
~1 week
Deep Learning — Goodfellow, Bengio & Courville
deeplearningbook.org (FREE PDF) | WHEN: Weeks 2-3 (parallel with coding Phase 2)
READ: Ch.6: Deep Feedforward Networks (backprop math, the rigorous version) | Ch.9: CNNs (architecture design for MFCC input) | Ch.7 Sections 7.1-7.3: Regularization
SKIP: Ch.14-20: VAEs, GANs, deep generative models, RL — not needed
Why: The math in FQT paper assumes you know Ch.6 & Ch.8. Read these before Phase 4.
3
~2 hours
Quantizing Deep CNNs — Krishnamoorthi (2018)
arXiv:1806.08342 (11 pages — FREE) | WHEN: Before Phase 4 (Week 8)
READ: Read FULLY — all 11 pages. Section 3.2: Per-channel quantization (= Eq.6-7 in Deutel) | Section 5: QAT vs PTQ comparison
SKIP: Nothing — it is only 11 pages
Why: Bridges theory to practice. Read this immediately before implementing calibrate.py.
4
~1 day
ARM CMSIS-NN Programmer Guide
developer.arm.com/documentation (FREE) | WHEN: Before Phase 5 (Week 11)
READ: arm_convolve_HWC_q7 reference | arm_fully_connected_q7 reference | arm_depthwise_separable_conv_HWC_q7 reference
SKIP: float16 and float32 sections (you are using q7 = int8 only)
Why: Every CMSIS-NN function call in inference.c needs the exact buffer layout from this guide.

## Slide 29
Required Courses — Exact Lessons & Learning Order
Do these in parallel with coding phases — not sequentially
1
~3 wks @ 5hr/wk
fast.ai — Practical Deep Learning Part 1
course.fast.ai (FREE) | WHEN: Weeks 1–3
DO: Lesson 1-3: PyTorch basics + image classification | Lesson 7: Training in depth | Lesson 8: Backprop from scratch — write it in pure Python — CRITICAL before Phase 3
SKIP: Lessons 9-10+ (NLP, diffusion — not needed)
Why: Lesson 8 gives you the intuition to implement rigl.py and fqt_sgd.py without getting lost.
2
~1 wk (sel.)
CS231n Stanford — Convolutional Neural Networks
YouTube: search 'CS231n 2017' (FREE) | WHEN: Weeks 1–4
DO: Lecture 4: Backprop & neural networks | Lecture 5: CNN architectures | Lecture 7: Training NN part 1 (SGD, momentum, LR schedules) | Lecture 8: Training NN part 2 (regularization, BatchNorm)
SKIP: Lectures 9-16 (RNNs, GAN, generative models, RL) — completely irrelevant
Why: Lecture 4 is the best 75-min explanation of backprop graphs — watch before writing any gradient code.
3
~4 wks @ 3hr/wk
deeplearning.ai — Neural Networks & Deep Learning (Course 1/5)
Coursera — Free audit (FREE) | WHEN: Weeks 2–5
DO: Week 1-4: ALL (neural network basics through deep networks) | Week 3-4: most critical — shallow to deep backprop, vanishing gradients
SKIP: Courses 3, 5 (structuring ML projects, sequence models — not needed for this thesis)
Why: Bridges Nielsen visuals to Goodfellow math. Do Week 4 programming exercises before starting Phase 3.
4
~1 day
numpy + scipy Tutorials — Sensor Data Processing
numpy.org/doc + scipy.org/doc (FREE) | WHEN: Start of Phase 2 (Week 3)
DO: numpy indexing + slicing | scipy.signal for windowing | sklearn metrics for 6-class confusion matrix
SKIP: Audio/speech tutorials (not relevant — your data is already in .npy sensor format)
Why: HAR .npy files are already segmented and normalized — dataset.py is simple numpy load + DataLoader wrapping.
5
~1 day
ARM — Getting Started with CMSIS-NN on Cortex-M
developer.arm.com/documentation (FREE) | WHEN: Start of Phase 5 (Week 11)
DO: Full CMSIS-NN quickstart guide | Search YouTube: 'STM32 X-CUBE-AI lab' — watch the hands-on lab video | Read STM32CubeIDE linker map tutorial to find RAM usage
SKIP: Float16 and TrustZone sections — using int8 only
Why: Before writing inference.c, you need to know the exact q7 buffer format ARM expects.

## Slide 30
Summary & Key Takeaways
1
FQT (Deutel et al.)
8-bit quantized training on Cortex-M MCUs is feasible. Key tools: quantized backprop (Eq.1-4), standardized SGD (Eq.8), dynamic sparse gradient updates (Eq.9). Results: 34.8% less RAM, 49% lower latency vs MCUNet.
2
RigL (Evci et al.)
Train sparse networks from scratch — no dense model ever needed. Drop by weight magnitude, Grow by gradient magnitude, use ERK distribution. Matches or beats dense-to-sparse pruning at 23% of training FLOPs.
3
Your Thesis Combination
RigL reduces parameter count -> FQT trains in 8-bit integers -> Result fits in 320 KB STM32 RAM. Activity recognition model adapts to new users entirely on-device.
4
Implementation Path
16 weeks: Setup -> UCI HAR data pipeline (raw sensor, no MFCC) -> Dense baseline -> RigL sparse training -> FQT+RigL in C framework -> STM32 on-device training -> Evaluation -> Thesis writing.
Thank you! Questions welcome.